Action Items from MARS Taskforce October 29, 2008

Discuss Response to Questions:

| Will the data put on the FTP site be raw or VEE’d? | AEP and Oncor Response: Will provide VEE data the next calendar day at 12:00:00 (noon). The VEE data will be posted to the FTP site and provided to ERCOT for processing CNP Response: Will post RAW data the next calendar day at 12:00:00 (noon). The RAW data will be updated on the 4th Day with VEE Data and will be available for CRs downloads. The VEE data/file on the 4th day will be sent to ERCOT for processing. TNMP Response: At this time, TNMP is currently too early into their AMS Project Plan to provide a response to this question. Consensus Statement: CR disputes, disagreements, or Data Extract Variances (DEVs) for AMS provisioned meters would not be based upon data provided on the TDSPs FTP Site. The Market should only rely on the data/files sent to ERCOT by the TDSP and ERCOT used that data for settlement. |
| --- | --- |
| If whole day is missing, post estimate reads, or post once data is available? | AEP, CNP and TNMP agree that the data would be posted once data is available. Data for an ESI ID will not be posted if there are any gaps in the intervals for the prior operating day for that ESI ID. Data will be posted at noon the day after the data becomes available. Oncor anticipates VEE processing after each operating day and providing the data daily CRs want the data the next day, even if there are gaps. AEP and Oncor Response: Since AEP and Oncor will provide VEE data the next calendar day then any missing data or gaps will be filled with Estimated (E) usage prior to posting the file to the FTP site on the next calendar day at noon. CNP Response: In the FTP file if any data is available for that day then that data will be provided in the file for the CRs and if no data is available for the whole day we will post file with all NULLs. If the data that is pulled for that day has gaps, CNP will fill those gaps with Nulls the next day to post the raw data for 12:00 noon. Once data is VEE on the fourth day, if gaps still exist those gaps will be updated with estimated usage then posted to the FTP site. TNMP Response: At this time, TNMP is currently too early into their AMS Project Plan to provide a response to this question. |
| Scenario 1: ESI ID is inadvertently switched and then returns to original CR. TDSP cancels/rebills usage. | Rep 1 is the rep of record. TDSP is providing Rep 1 with usage information – in the form of monthly 867_03s and .lse files on the FTP site. Rep 2 inadvertently obtains the ESI ID from Rep 1. (Rep 1 receives an 867_03F closing out their service instance. Rep 2 receives an 867_04.) TDSP provides Rep 2 with usage information – in the form of monthly 867_03s and .lse files on the FTP site. MarkeTrak Inadvertent issue is logged. (either rep can submit issue) CR/TDSP resolution is for the Losing CR, Rep 1, to submit a backdated Move In for 1 day after Rep 2 obtained the ESI ID. Rep 1 submits Move In (Date Wanted (DTW) is 1 day after REP 2 obtained the ESI ID) TDSP cancels any monthly 867_03s sent to Rep 2. . TDSP completes REP 1 for requested date (1 day after Rep 2 obtained the ESI ID). (REP 1 receives an 867_04. REP 2 receives an 867_03F.) TDSP sends rebill 867_03s to Rep 1-. These transactions are forwarded to Rep 1. TDSP creates updated .lse files with usage for all the days since the backdated Move In with Rep 1’s DUNS number and places these on the FTP site for Rep 1. (These transactions do not need to be sent to ERCOT unless an ERCOT required value in the file has changed.) Can the CRs just download the data from ERCOT’s web services instead of relying on the FTP site? CRs – will web services work? TDSPs – can the new .lse files be provided on FTP? Taskforce Questions: Will the .lse files created for Rep 2 remain on the FTP site? They will remain until they roll off at 10 days. What if the ESI ID is returned to the original Rep prior to a monthly 867_03 being sent? In that case the gaining rep will not have received a monthly 867_03 to be cancelled. Will they have to use the 814_06 and 867_03F to know that the usage is no longer theirs? TDSPs Consensus Statement (AEP, CNP, Oncor, and TNMP) : Since this occurrence would be so infrequent we would like to encourage the CRs to pull this data from ERCOT’s web services and from the 867_03(F) transaction they receive. Also if the CRs are pulling files daily they may already have the 15 minute interval for the date(s) where they where REP of Record. |
| Meter Offset (what is the value?) – does it need to be included in FTP or ERCOT file (item #5 in LSE.file Format) | ERCOT’s Response: Not used by ERCOT Values currently in draft file format: Default = 0 Non-negative numeric Max = 999999999999999.9999 TDSPs Consensus Statement (AEP, CNP, Oncor, and TNMP) : Meter Offset (item #5 in LSE.file format) is not applicable to AMS meters nor needed for TDSP billing of AMS enabled premises, therefore TDSPs recommend that this value be removed from the FTP and ERCOT files. |
| Pulse Offset (what is the value?) – does it need to be included in FTP or ERCOT’s file (item #7 in LSE.file Format) | ERCOT’s Response: Not used by ERCOT Values currently in draft file format: Default = 0 Non-negative numeric Max = 999999999999999.9999 TDSPs Consensus Statement (AEP, CNP, Oncor, and TNMP) : Pulse Offset (item #7 LSE.file format) is not applicable to AMS meters nor needed for TDSP billing of AMS enabled premises, therefore TDSPs recommend that this value be removed from the FTP and ERCOT files. |

Use Case Number:  15

| High Level Description | Scenario detailing how switching will work on an AMS meter. |
| --- | --- |
| Requirement | No ERCOT system changes required for this use case. |
| Pre-Conditions/Trigger | Premise has an AMS meter provisioned. CRs – Do you want Move Outs (to de-energized) occurring at midnight? TDSPs – Can you do move outs at midnight? TDSPs Consensus Statement (AEP, CNP, Oncor, and TNMP) : Move-In(s) (De-energized premise with AMS “Provisioned” Meter: Since this is the interim solution that we are solving for the TDSPs agree our current processes will stay in place for Move-In(s) with an AMS “provisioned” meter, meaning we will energize the meter and obtain the start reading anytime during normal business hours on the scheduled Move-In date. TDSPs recommend that a long term solution should be discussed in the Market that takes into consideration all the issues that a change to the current processes and business practices will impact. Move-Out (Energized premise with AMS “Provisioned” Meter: Since this is the interim solution that we are solving for the TDSPs agree our current processes will stay in place for Move-Out(s) with an AMS “provisioned” meter, meaning we will de-energize the meter and obtain the stop/end reading anytime during normal business hours on the scheduled Move-Out date. TDSPs recommend that a long term solution should be discussed in the Market that takes into consideration all the issues that a change to the current processes and business practices will impact. Move-In Force Off and Switch: The TDSP agree that in these scenarios we will obtain a reading at 00:00:00 on the scheduled Move-In/Force Off or Switch dates. CRs should be aware that 100% guarantee of always executing at 00:00:00 is not possible. |
| Data | Rep 1 | Rep 2 |
| Service History | 1/1/2008 00:00:00 – 7/21/2008 23:59:59 | 7/22/2008 00:00:00 - |
| 867_03 NIDR | Start - 06/22/2008 Stop - 07/22/2008 This transaction will contain the usage through 14:00:00 on 7/22/2008 | Start - 07/23/2008 Stop - 08/22/2008 This transaction will contain the usage starting at 14:00:00 on 7/22/2008 |
| LSE Files on FTP Site | Last .lse file provided to Rep 1 ends at 7/21/2008 23:59:59 | Rep 2’s first .lse file begins at 7/22/2008 00:00:00 |
| Result | Rep 1 will not be able to add up the interval data to equal the 867_03F. The interval data from 7/22/2008 will be missing. | Rep 2 will not be able to add up the interval data to equal the 867_03. The interval data from all of 7/22/2008 will be included even though only part of it was included in the 867_03. |