2705 West Lake Drive

Taylor, Texas 76574

(512) 248-6800

HTTP://WWW.ERCOT.COM

Methodologies for Determining Actual Fuel Prices Incurred by QSEs for RUC Commitments

V0.02

March 30, 2011

Table of Contents

Section 1 – Introduction	3

Section 2 – Statement of Purpose	3

Section 3 –Methodology for Determining the SUPR and MEPR	3

# Section 1 – Introduction

Per Nodal Protocol Section 9.14.7, Disputes for RUC Make-Whole Payment for Exceptional Fuel Costs, QSEs may recover the actual cost of fuel paid for providing a Reliability Unit Commitment (RUC) service if the actual fuel price is higher than FIP, FOP, or 1.5, for solid fuel, plus VOX (value of X), if applicable.  This white paper describes the methodology used by ERCOT to determine the Startup Price (SUPR) and Minimum Energy Price (MEPR) when a QSE submits a dispute to recoup actual fuel prices.

# Section 2 – Statement of Purpose

As amended by NPRR174, FIP Modifications in Verifiable Startup and Minimum Energy Cost and Recovery of Exceptional Fuel Costs During RUC Intervals, and NPRR212, Disputing Fuel Oil Price (FOP) Costs, Section 9.14.7 allows the recovery of the actual fuel price paid whenever a Resource receives a RUC commitment.  In order to compensate the QSE for the incremental fuel cost, ERCOT will recalculate the RUC Guarantee using the actual fuel price paid.  However, given that QSEs may submit Startup and Minimum Energy Offers that are below the Offer caps, ERCOT must make some assumptions on what the QSEs “actually” offered since the Offers are composed of the fuel rate, fuel price and O&M values.  Section 3 below describes two scenarios that may occur.

# Section 3 –Methodology for Determining the SUPR and MEPR

There are four possible scenarios that may arise when QSEs dispute additional fuel compensation.  This white paper only addresses two of the scenarios.

- No approved Verifiable Costs and approved Offers

- Approved Verifiable Costs and approved Offers

Scenario 1: No approved Verifiable Costs and Approved Offers

MEO ($/MWh) = HROffer * FIP/FOP

Or

HROffer (MMBtu/MWh) = MEO / (FIP/FOP)

Where,

MEO = Minimum Energy Offer

HROffer = Heat Rate submitted with Minimum Energy Offer

The new calculated Offer using the actual fuel price is

MEONew ($/MWh) = HROffer * AFPrice

And

MEPRNew ($/MWh) = MEONew ($/MWh)

Where,

MEPRNew =  New Minimum Energy Price

AFPrice = Actual price of fuel paid

Note:  The calculated Offered Heat Rate (HROffer) is used instead of the Generic Heat Rate otherwise the Resource could be paid more than what it Offered.  The maximum (Cap) Heat Rate value the QSE can submit with an Offer is the Generic Heat Rate.  Since generic startup costs do not include fuel, the SUPR is not calculated and additional compensation is only based on the MEPR.

Scenario 2: Approved Verifiable Costs and Approved Offers

If Offers < Cap

When offers are less than the Cap, it is assumed that the QSE has used a low O&M (even negative) value to construct its Offer since it is unlikely a lower fuel rate or price was used.

Startup

SUO ($) = VC Fuel * FIP/FOP + O&MNew

Or

O&MNew ($) = SUO - VC Fuel * FIP/FOP

Where,

SUO = Startup Offer

VC Fuel = approved fuel rate

Note:  the O&MNew could be negative when the SUO is  below the product of VC Fuel * FIP/FOP

Or

SUONew ($) = VC Fuel * AFPrice + O&MNew

And

SUPRNew ($) = SUONew ($)	Where

SUPR = Startup Price

Minimum Energy

MEO ($/MWh) = HRVC * FIP/FOP + O&MNew-LSL

Or

O&MNew-LSL ($/MWh) = MEO – HRVC * FIP/FOP

Where,

HRVC = approved heat rate

Note:  the O&MNew-LSL could be negative when the MEO is below the product of HRVC * FIP/FOP

Then

MEONew ($/MWh) = HRVC * AFPrice + O&MNew-LSL

And

MEPRNew ($/MWh) = MEONew ($/MWh)

If the Resource does not have approved O&M at Minimum Energy, then HRVC is replaced with HROffer since it is assumed the Resource did not lowered the fuel price.

MEO ($/MWh) = HROffer * FIP/FOP

Or

MEONew ($/MWh) = HROffer * AFPrice

Where,

HROffer = MEO / (FIP/FOP)

And

MEPRNew ($/MWh)  = MEONew ($/MWh)