| RRGRR Number | 009 | RRGRR Title | Adding Voltage Limit Sets, Relay Loadability, MLSE, and GMD Data |
| --- | --- | --- | --- |
| Date Posted | February 26, 2016 |
| Requested Resolution | Normal |
| Resource Registration Glossary Sections Requiring Revision | Section 2, Resource Registration Glossary |
| Related Documents Requiring Revision/Related Revision Requests | 046PGRR, Addition of Geomagnetically-Induced Current Model Building Requirements |
| Revision Description | This Resource Registration Glossary Revision Request (RRGRR) adds three categories of data: Voltage limits are needed for Resources to indicate that their substation transmission level equipment is limited to a certain range of voltages. The relay loadability limits indicate the limits of loading for certain equipment. Geomagnetic Disturbance is a newly emphasized risk to the grid. The addition of geomagnetically-induced currents and the presence of blocking devices will allow for the study of any vulnerability due to Geomagnetic Disturbance. The addition of a Most Limiting Single Element (MLSE) allows a Resource Entity to identify an MLSE even if that element affects a line not owned by a Resource Entity. |
| Reason for Revision | Addresses current operational issues. Meets Strategic goals (tied to the ERCOT Strategic Plan or directed by the ERCOT Board). Market efficiencies or enhancements Administrative Regulatory requirements Other: (explain) (please select all that apply) ERCOT needs to be able to monitor and secure Resource Entity equipment with a VoltageLimitSet (High & Low) for both Normal and Emergency conditions (in per unit voltage). Per Nodal Protocol Section 3.10, Network Operations Modeling and Telemetry. Relay Loadability Limits – TPL001-4 (Transmission System Planning Performance Requirements) requires ERCOT to study Bulk Electric System for performance under certain conditions. TPL-007-1 (Transmission System Planned Performance for Geomagnetic Disturbance Events) will require ERCOT to study the Bulk Electric System for vulnerability to Geomagnetic Disturbances. ERCOT anticipates that this standard will pass. The MLSE will allow a Resource Entity to identify a limitation that affects equipment that they do not own. This will allow ERCOT to apply the correct limits to Transmission Elements. |
| Business Case | The inclusion of this information into the Resource Asset Registration process will allow ERCOT to study and better protect Resource equipment and comply with new or revised NERC standards. |

| Sponsor |
| --- |
| Name | Art Deller |
| E-mail Address | Art.deller@ercot.com |
| Company | ERCOT |
| Phone Number | 512-248-6505 |
| Cell Number |  |
| Market Segment | Not applicable |

| Market Rules Staff Contact |
| --- |
| Name | Lindsay Butterfield |
| E-Mail Address | Lindsay.Butterfield@ercot.com |
| Phone Number | 512-248-6521 |

Comments

The proposed changes to Section 2, Resource Registration Glossary, are included in the spreadsheet 009RRGRR-01a Adding Voltage Limit Sets, Relay Loadability, MLSE and GMD data 022616.

Proposed Guide Language Revision

# 2	Resource Registration Glossary

See electronic Microsoft Office Excel© file on the ERCOT website posted with the Resource Registration Glossary.