## Slide 1
Multi-Interval Real-Time Market Update to SAWG
August 15, 2016

## Slide 2: Refresher on the MIRTM Process
MIRTM six 5-minute intervals (30 minutes total) with separate commitment and dispatch
8:40 8:45 8:50 8:55 9:00 9:05 9:10 9:15 9:20 9:25 9:30 9:35
Intervals where ONLY Commitment Instructions are binding and the LMPs and MW awards (energy, AS) are indicative
Interval where the LMPs, MW awards (energy, AS) and Commitment Instructions are ALL binding commitment instructions
Sequence of Multi-Interval RT Markets
Analysis window of rolling 30 minutes
RT Market Execution: Depicts the start and end times of the clearing process and the length of symbol is indicative of maximum time allowed to clear market
Dispatch Run & Pricing run
Dispatch Run & Pricing Run
Binding commitments for ALL intervals
1st Interval Binding Base Point & Binding LMPs
Note: The introduction of the Binding Dispatch/Base Point run while eliminating make-Whole payments to Generation Resources due to binding ramp constraints, can however, lead to missed commitments or too early decommitments/recalls. The assumption is that the benefits of eliminating this category of make-whole payments outweighs the disadvantages of missed commitments or too early decommitments/recalls.

## Slide 3: Overview of Recent Activity
Implement Dispatch module
Implement Pricing module
Developed Three part offers (TPO) based on average Verifiable Costs and unit HSL
Developed Single part offers (SPO) from TPO allocating start costs over min up time
Allowed for Wartsila units to have zero start time and zero min off time (allows fast ramping resources to meet demand in same interval)
Studied the following dates:7/1/2015, 8/11/2015, 8/13/2015, 11/11/2015

## Slide 4: Today’s Agenda
Refresher on study inputs
For study day 8/13/2015 review and compare all of the Separate Commitment and Dispatch MIRTM runs listed on the next slide
For remaining three study days
  7/1/2015 – Luminant request (Volatile wind, little congestion, low system lambda)
  8/11/2015 - Luminant request (Little congestion, low dispatchable capacity)
  11/11/2015 - ERCOT (New STLF over forecasts load)
  Compare two runs:
    Separate Commitment and Dispatch (3PO) (fast responding resources and load)
    Separate Commitment and Dispatch (LOAD) (fast responding resources modeled as production i.e. not committable by MIRTM)

## Slide 5: Study Runs
For the 8/13 run we will step incrementally through the progression of studies as follows:
Production SCED
Sequential SCED
MIRTM with Separate Commitment and Dispatch:
  Loads only with QSGR not committable to mimic production (LOAD)
  QSGRs have Production offers with single part offers (SPO Prod. SCED EOCs)
  QSGRs have three-part offer based on average Verifiable Costs (3PO)
  QSGRs have single-part offer based on average Verifiable Costs (SPO)
  Note: we could come back at a later date with a comparison between MIRTM Combined Commitment and Dispatch and MIRTM Separate Commitment and Dispatch. It was too much data to show in one session.

## Slide 6: Study Process
Determine the study period based on the day of interest and run a sequential SCED for the entire study period using the Energy Offers from actual Real Time SCED runs.
Sequential SCED considered the “baseline” that simulates all resources following base points while the GTBD mimics the production case.
Run MIRTM Separate Commitment and Dispatch with different offer structures (SPO Prod. SCED EOCs, 3PO, SPO) as inputs while the GTBD mimics the production case.
Use new STLF and Wind Persistence to “look ahead” 30 minutes to determine if commitments needed

## Slide 7: Study Process
Calculate Production Costs: Four Components
  Generation Costs: Integrate Step 2 EOC from LSL to BP + Power Balance Violation
  Transmission Penalty Cost: Violated MW * Shadow Price
  QSGR Startup/Mingen Cost: Startup and Minimum Energy Costs
  Blocky Load Cost: Bid Price * Commit MW
Calculate Make Whole
  QSGR Make whole across entire study period
    Prod. SCED & Seq. SCED: Emergency Operations QSGR payments (Per 6.6.9 (3))
    MIRTM: Max(0,QSGR Revenue - QSGR Verifiable Cost)
  Blocky Load Make whole across entire study period
    MIRTM: Max(0,[Binding LMP * Commit MW] - [Bid Price * Commit MW])
Notes: QSGR revenue:
(Binding LMP + ORDC Online Price Adder + Pricing Run Price Adder) * Binding Base Point of Committable QSGR Unit List
QSGR Verifiable cost:
QSGR Verifiable Cost Above LSL - Integrate Input EOC or Verifiable Cost EOC (if no QSGRs in MIRTM) from LSL to BP of Committable QSGR Unit List
plus
QSGR Startup/Mingen Cost of Committable QSGR Unit List - Startup and Minimum Generation Costs of Committable QSGR Unit List

## Slide 8: Simulation Assumptions – Blocky Load Resources
Offers were received for 12 Blocky Loads from DSWG
A total of 366 MW split between the load zones (each zone has 12 resources)

## Slide 9: Simulation Assumptions – Fast Generation Resource Temporal Constraints
All Resources that are Quick Start qualified are considered “fast responding resources”. If the Resource was “OUT” or “ONTEST” during the study period they are not considered as “committable” Gas Turbines (36 units)
Reciprocating Engines (3 units)
Minimum On Time | Minimum Off Time | Hot to Intermediate Time | Intermediate to Cold Time | Cold StartUp Time | Intermediate StartUp Time | Hot StartUp Time
0 min. | 0 min. | 0 min. | 0 min. | 0 min. | 0 min. | 0 min.
Wartsilas (4 units)

## Slide 10: Simulation Assumptions – Fast Responding Resources
Four average Verifiable Costs groups were identified.
Each Fast Responding Resources is assigned a group cost based on HRL/LSL
The Single Part offer is structured in order to recover Start Up and Minimum Energy cost over the Minimum On time
Minimum EOC is $75 if Resource had Non-Spin responsibility during study period
Res Type | HRL (MW) | LRL (MW) | Seasonal LSL (MW) | Startup Cost ($) | Min-Energy Price ($/MWh) | Min EOC ($/MWh) | Max EOC ($/MWh) | Single Part Cost ($/MWh)
SCLE90 | 54.0 | 10.0 | 13.0 | 4,322.05 | 52.39 | 30.86 | 33.91 | 1,287.26
SCLE90 | 60.0 | 0.0 | 12.0 | 3,448.99 | 48.85 | 28.47 | 31.05 | 1,198.51
SCLE90 | 95.0 | 0.0 | 41.0 | 6,058.75 | 56.12 | 40.35 | 41.88 | 647.21
DSL | 8.9 | 6.0 | 6.0 | 962.21 | 39.93 | 34.84 | 39.79 | 1,964.34

## Slide 11: Other Assumptions – Days Analyzed
  The Capacity from all Fast Responding Resources is considered online in MIRTM study runs; this has the impact of changing the ORDC calculation slightly; however, the resource capacity is only shifted from offline to online.
  The Block Load Resources are considered “new” Resources which increases the RTOLCAP and shifts the curve to the right by 366MW.
  Keep this in mind when comparing the ORDC price adder revenues across the Production SCED, Sequential SCED, and MIRTM study runs.
  The Reliability Deployment Price Adder in MIRTM treats the deployment by ERCOT as a “deployment event” therefore MIRTM may find a RTDP when Production and Sequential SCED did not.

## Slide 12: Study Day: August 13, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_SPO_PROD_EOC | MIRTM_3PO | MIRTM_SPO
Generation Cost | 4797543.2906 | 4511059.4623 | 4497899.0416 | 4442096.4527 | 4533296.9168 | 5072238.6267
Transmission Penalty Cost | 42320.8333 | 39439.0148 | 39198.0202 | 21928.204 | 7223.5526 | 117641.4014
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 177305.0123 | 362737.7094 | 937656.5265
Blocky Load Cost | 0 | 0 | 3562.5 | 2781.25 | 0 | 141795.8333

## Slide 13: Study Day: August 13, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_SPO_PROD_EOC | MIRTM_3PO | MIRTM_SPO
Average System Lambda | 93.5205 | 86.0555 | 85.7228 | 81.8263 | 69.0051 | 485.1258
Average RTORPA | 90.4866 | 57.3711 | 26.1343 | 25.6677 | 26.1336 | 21.5396
Average RTRDPA | 0 | 0 | 0.2021 | 0.3277 | 0.7095 | 18.3349
Average RTOFFPA | 71.2621 | 47.9189 | 23.516 | 23.1791 | 23.6214 | 19.5432
Increase in prices due to offer assumptions (see slide 10)

## Slide 14: Study Day: August 13, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_SPO_PROD_EOC | MIRTM_3PO | MIRTM_SPO
QSGR Makewhole | 16.61 | 16.61 | 0 | 0 | 0 | 0
Blocky Load Makewhole | 0 | 0 | 0 | 0 | 0 | 0
Zero Make Whole

## Slide 15: Study Day: August 13, 2015 Cost and Revenue

## Slide 16: Study Day: August 13, 2015 HDL-GTBD, SL

## Slide 17: Study Day: August 13, 2015 Commitment Summary

## Slide 18: Study Day: July 1, 2015
  7/1/2015 – Luminant request (Volatile wind, little congestion, low system lambda)

## Slide 19: Study Day: July 01, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | -606109.3782 | -609429.9318 | -610763.2004 | -600711.3099
Transmission Penalty Cost | 0 | 0.0059 | 0 | 0
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 0
Blocky Load Cost | 0 | 0 | 0 | 0

## Slide 20: Study Day: July 01, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 24.8437 | 24.8727 | 24.8724 | 24.9347
Average RTORPA | 0 | 0 | 0 | 0
Average RTRDPA | 0 | 0 | 0 | 0
Average RTOFFPA | 0 | 0 | 0 | 0

## Slide 21: Study Day: July 01, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 0 | 0 | 0 | 0
Blocky Load Makewhole | 0 | 0 | 14 | 0
Zero Make Whole

## Slide 22: Study Day: July 1, 2015 – Cost and Revenue

## Slide 23: Study Day: July 1, 2015 – HDL-GTBD, SL

## Slide 24: Study Day: July 1, 2015 – Commitment Summary
Zero Commitments

## Slide 25: Study Day: August 11, 2015
  8/11/2015 - Luminant request (Little congestion, low dispatchable capacity)

## Slide 26: Study Day: August 11, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | 4068477.83 | 4061046.7 | 4070382.34 | 4162934.26
Transmission Penalty Cost | 845.83 | 847.15 | 848.42 | 848.96
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 464463.6
Blocky Load Cost | 0 | 0 | 0 | 0

## Slide 27: Study Day: August 11, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 49.73 | 49.62 | 49.64 | 51.66
Average RTORPA | 64.91 | 46.71 | 20.86 | 20.5
Average RTRDPA | 0 | 0 | 0 | 1.27
Average RTOFFPA | 45.74 | 34.48 | 16.97 | 16.68

## Slide 28: Study Day: August 11, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 26.94 | 26.94 | 0 | 0
Blocky Load Makewhole | 0 | 0 | 0 | 0

## Slide 29: Study Day: August 11, 2015 – Cost and Revenue

## Slide 30: Study Day: August 11, 2015 – HDL-GTBD, SL

## Slide 31: Study Day: August 11, 2015 – Commitment Summary

## Slide 32: Study Day: Nov 11, 2015
  11/11/2015 - ERCOT (New STLF over forecasts load)

## Slide 33: Study Day: Nov 11, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | -2414334.8031 | -2446877.2077 | -2435333.4584 | -2380936.6978
Transmission Penalty Cost | 9858.3333 | 0.081 | 0 | 43962.9929
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 169257.6689
Blocky Load Cost | 0 | 0 | 0 | 0

## Slide 34: Study Day: Nov 11, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 34.97 | 26.3053 | 23.7557 | 25.4511
Average RTORPA | 0.9121 | 1.0002 | 0.2739 | 0.1994
Average RTRDPA | 0 | 0 | 0 | 2.1662
Average RTOFFPA | 0.4893 | 0.5215 | 0.1741 | 0.1639

## Slide 35: Study Day: Nov 11, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 8093.28 | 8093.28 | 0 | 76488.7517
Blocky Load Makewhole | 0 | 0 | 0 | 0

## Slide 36: Study Day: Nov 11, 2015 – Cost and Revenue

## Slide 37: Study Day: Nov 11, 2015– HDL-GTBD, SL

## Slide 38: Study Day: Nov 11, 2015 – Commitment Summary

## Slide 39: Appendix

## Slide 40: Study Day: August 13, 2015 MIRTM Load only

## Slide 41: Study Day: August 13, 2015 MIRTM Load only

## Slide 42: Study Day: August 13, 2015 MIRTM Load only

## Slide 43: Study Day: August 13, 2015 MIRTM Prod EOC

## Slide 44: Study Day: August 13, 2015 MIRTM Prod EOC

## Slide 45: Study Day: August 13, 2015 MIRTM Prod EOC

## Slide 46: Study Day: August 13, 2015 MIRTM 3PO

## Slide 47: Study Day: August 13, 2015 MIRTM 3PO

## Slide 48: Study Day: August 13, 2015 MIRTM 3PO

## Slide 49: Study Day: August 13, 2015 MIRTM SPO

## Slide 50: Study Day: August 13, 2015 MIRTM SPO

## Slide 51: Study Day: August 13, 2015 MIRTM SPO

## Slide 52: Study Day: July 1, 2015 – MIRTM Load Only

## Slide 53: Study Day: July 1, 2015 – MIRTM Load Only

## Slide 54: Study Day: July 1, 2015 – MIRTM Load Only

## Slide 55: Study Day: July 1, 2015 – MIRTM 3PO

## Slide 56: Study Day: July 1, 2015 – MIRTM 3PO

## Slide 57: Study Day: July 1, 2015 – MIRTM 3PO

## Slide 58: Study Day: August 11, 2015 – MIRTM Load only

## Slide 59: Study Day: August 11, 2015 – MIRTM Load only

## Slide 60: Study Day: August 11, 2015 – MIRTM Load only

## Slide 61: Study Day: August 11, 2015– MIRTM 3PO

## Slide 62: Study Day: August 11, 2015– MIRTM 3PO

## Slide 63: Study Day: August 11, 2015– MIRTM 3PO

## Slide 64: Study Day: Nov 11, 2015 – MIRTM Load only

## Slide 65: Study Day: Nov 11, 2015– MIRTM Load only

## Slide 66: Study Day: Nov 11, 2015 – MIRTM Load only

## Slide 67: Study Day: Nov 11, 2015 – MIRTM 3PO

## Slide 68: Study Day: Nov 11, 2015 – MIRTM 3PO

## Slide 69: Study Day: Nov 11, 2015 – MIRTM 3PO

## Slide 70: Study Day: Nov 27, 2015 – MIRTM Load only

## Slide 71: Study Day: Nov 27, 2015– MIRTM Load only

## Slide 72: Study Day: Nov 27, 2015 – MIRTM Load only

## Slide 73: Study Day: Nov 27, 2015 – MIRTM 3PO

## Slide 74: Study Day: Nov 27, 2015 – MIRTM 3PO

## Slide 75: Study Day: Nov 27, 2015 – MIRTM 3PO