## Slide 1
Options to Collect Transmission Outage Statistics
(May 17 2017, PLWG)

## Slide 2: Introduction
ERCOT presented probabilistic transmission planning efforts at the Nov-2016 PLWG:
  http://www.ercot.com/calendar/2016/11/16/81140-PLWG
Outage statistics of system elements is one of the key components necessary to implement probabilistic transmission planning approach.
ERCOT is presenting four potential options for collecting outage statistics of transmission elements. ERCOT is seeking feedback from PLWG.

## Slide 3: Options for Collecting Transmission Outage Statistics
Option 1: Using Nation-wide Generic Data
  NERC Transmission Availability Data System (TADS)
    Outage statistics of transmission elements above 200 kV since 2008
    Outage statistics of transmission elements for 100-199 kV and less than 100 kV (BES only) since 2015
  It is not region-specific outage data. Ignores variability due to environmental conditions and geographic locations.
  Due to confidentiality issue, ERCOT is not able to access the detail of the outage data in the NERC TADS.

## Slide 4: Options for Collecting Transmission Outage Statistics
Option 2: Outage Data in ERCOT’s Outage Scheduler
  ERCOT Nodal Protocol Section 3.1.4.5(2) requires TSP and QSE to enter Forced Outage occurred in Real-Time into the ERCOT Outage Scheduler.
  Applicable to Forced Outage with duration more than 2 hours only. Currently, forced outages have to be submitted in present time because outage scheduler does not accept the timestamp in past.
  Revision of Nodal Protocol will be needed under Option 2.
    To collect more comprehensive outage data (e.g. duration >= 1 minute)
    To have the information of a forced outage in a format consistent with the ERCOT Nodal Protocol Section 3.1.5.9 (Information for Inclusion in Transmission Facilities Outage Requests: Planned or Maintenance Outage)
  Conversion from node-breaker outage model to bus-branch outage model will be needed.

## Slide 5: Options for Collecting Transmission Outage Statistics
Option 3: Outage Data from TSPs
  Since TSPs submit outage data for NERC TADS, ERCOT assumes that each TSP can provide historical outage data to ERCOT as requested (e.g. once every two year or as needed for a RPG review).
    Example outage statistics – Transmission Line
    Example outage statistics – Transformer
  More detailed data by weather zone, county and fault type (e.g. P1-P7) will be very helpful to estimate region-specific outage statistics.
Min kV | Max kV | Type | Frequency (Occurrence/100miles.year) | Duration (Hr/Occurrence)
300 | 399 | Overhead | 1.165 | 22.918
Min kV | Max kV | Frequency (Occurrence/year) | Duration (Hr/Occurrence)
300 | 399 | 0.1317 | 459.6

## Slide 6: Options for Collecting Transmission Outage Statistics
Option 4: Outage Data from TRE
  ERCOT plans to contact TRE for possibility of obtaining the NERC data associated with ERCOT in an aggregated level because ERCOT is not allowed to access the detail of NERC data submitted by TOs and GOs.
  If Option 4 is feasible, it will address the issue (region-specific data) with Option 1.
  Data may not be available for the voltage class less than 200 kV.

## Slide 7: Summary
 | Option 1: Nation-Wide Generic Data | Option 2: Outage Data in ERCOT’s Outage Scheduler | Option 3: Outage Data from TSPs | Option 4: Outage Data from TRE
ERCOT Region-specific data (e.g. by weather zone)? | No | Yes | Yes | Maybe
100 kV and above? | Yes (since 2015) | Yes | Yes | Yes (since 2015)
Possible NPRR revision? | No | Yes | Maybe | No
Need for converting Node-breaker to Bus-branch model? | No | Yes | No | No
Any details regarding fault type of TPL-001-4 | No | Maybe | Maybe | No

## Slide 8: Next Steps
Stakeholder’s to review the options
Send your feedback to sunwook.kang@ercot.com
ERCOT will review your feedback for implementation of the option(s).