## Slide 1: Panhandle Bus Definition
QMWG
June 5, 2017

## Slide 2: Purpose
NPRR817, Create a Panhandle Hub, is under discussion and appears to have significant support; however, the confidence in the Hub definition is not strong. This analysis aims to provide options for ERCOT stakeholders to consider.
Disclaimer – this is the independent work of Megawatt Analytics, LLC and is not at the behest of any stakeholder and certainly should not be interpreted as such.

## Slide 3: Rules of Hubs
Protocols
  List of busses cannot be modified unless physically removed (3.5.1(2))
  Perpetual (2.1)
  Simple averages – quantity of generation or load at bus is irrelevant. (3.5.2)
Rules
  Average price of aggregated nodes (§25.501 (g))

## Slide 4: Patton Hub Recommendations
Avoid intra-hub congestion
  The day-ahead market model should be used to test the definition of the hub by submitting large net energy purchases and sales at the hub location under a defined range of market conditions
The nodes selected for use in the hub should be electrically similar and have a relatively stable price relationship in aggregate
  Resource node price correlations are strong, proposed hub bus correlations could be tested
Use consistent weighting of nodes between definition of the hub and the distribution methodology
  Using non-energy weighted simple average is consistent with distribution methodology ( 4.5.1 (6) )
Notes: http://megawattanalytics.com/storage/app/media/papers/TNTWhitepaperComments_PotomacEconomics-06240.pdf
4.5.1
(6) ERCOT shall allocate offers, bids, and source and sink of CRRs at a Hub using the distribution factors specified in the definition of that Hub in Section 3.5.2, Hub Definitions.

## Slide 5: Methodology for Hub Analysis
Assume Panhandle GTC should be the basis for Hub definition;
Find SCED interval with only Panhandle GTC binding;
Sort using “LMPs by Electrical Bus” report;
Map electrical bus to substations using:
  Settlement Points List and Electrical Buses Mapping
  ERCOT Steady State Planning Data Dictionary
  Day-Ahead PSS-E Network Operations Model and Supporting Files
Notes: 0800 4/27/17

## Slide 6: Raw Result- 30 Busses
ALIBATES
BRISCOE
ASTRA
ALN_CRK
CTT_GRAY
COTPLNS
GRANDVW1
CTT_CROS
HRFDWIND
LHORN_N
MIAM1
MARIAH
PH1
OGALLALA
W_CW_345
AEEC
ABERNATH
AJ_SWOPE
PH2
SSPURTWO
RAILHEAD
ROUTE_66
SALTFORK
SPLAIN1
SPLAIN2
TULECNYN
TESLA
WAKEWE
WINDMILL
WHIT_RVR
ABERNATH
AEEC
AJ_SWOPE
ALIBATES
ALN_CRK
ASTRA
BRISCOE
COTPLNS
CTT_CROS
CTT_GRAY
GRANDVW1
HRFDWIND
LHORN_N
MARIAH
MIAM1
OGALLALA
PH1
PH2
RAILHEAD
ROUTE_66
SALTFORK
SPLAIN1
SPLAIN2
SSPURTWO
TESLA
TULECNYN
W_CW_345
WAKEWE
WHIT_RVR
WINDMILL

## Slide 7: Pare by Protocol?
Electrically Similar Settlement Points
  Two or more distinct Settlement Points that are either mapped to the same electrical location in a market model or are mapped to locations that are connected by a transmission element with a reactance of less than 0.0005 per unit.
Notes: Chapter 2, Definitions

## Slide 8: Remove E.S.P. : 23 Busses
ALIBATES
ASTRA
ALN_CRK
CTT_GRAY
GRANDVW1
CTT_CROS
LHORN_N
MIAM1
MARIAH
OGALLALA
W_CW_345
ABERNATH
AJ_SWOPE
PH2
RAILHEAD
ROUTE_66
SPLAIN1
SPLAIN2
TULECNYN
TESLA
WINDMILL
WHIT_RVR
SSPURTWO
ABERNATH
AJ_SWOPE
ALIBATES
ALN_CRK
ASTRA
CTT_CROS
CTT_GRAY
GRANDVW1
LHORN_N
MARIAH
MIAM1
OGALLALA
PH2
RAILHEAD
ROUTE_66
SPLAIN1
SPLAIN2
SSPURTWO
TESLA
TULECNYN
W_CW_345
WHIT_RVR
WINDMILL

## Slide 9: E.S.P. Trimmings
Raw Bus | Reactance | E.S.P. Bus
AEEC | 0.00006 | ABERNATH
SALTFORK | 0.00001 | ALN_CRK
BRISCOE | 0.00032 | TULECNYN
COTPLNS | 0.00001 | WHIT_RVR
HRFDWIND | 0.00001 | WINDMILL
PH1 | 0.00039 | RAILHEAD
WAKEWE | 0.00048 | W_CW_345
These changes appear to be reasonable, but note PH1 to Railhead included, but PH2 is not.

## Slide 10: E.S.P. on the Margin
Raw Bus | Intuitive Bus | Reactance
GRANDVW1 | ALIBATES | 0.0005
SPLAIN1 | WHIT_RVR | 0.00051
OGALLALA | WINDMILL | 0.0006
RAILHEAD | CTT_GRAY | 0.0006
ROUTE_66 | ALIBATES | 0.0006
ASTRA | WINDMILL | 0.00069
LHORN_N | TULECNYN | 0.0008
PH2 | RAILHEAD | 0.00085
MIAM1 | CTT_GRAY | 0.00129
SPLAIN2 | WHIT_RVR | 0.00143
MARIAH | WINDMILL | 0.00161
SSPURTWO | AJSWOPE | 0.00376
Some of these are reasonable, but note GRANDVW1 is on the margin, SPLAIN1 is close, and PH2 does not qualify while its sister bus did.

## Slide 11: E.S.P. – Remove Radial: 11 Busses
ALIBATES
ASTRA
ALN_CRK
CTT_GRAY
GRANDVW1
CTT_CROS
LHORN_N
MIAM1
MARIAH
OGALLALA
W_CW_345
ABERNATH
AJ_SWOPE
PH2
RAILHEAD
ROUTE_66
SPLAIN1
SPLAIN2
TULECNYN
TESLA
WINDMILL
WHIT_RVR
SSPURTWO
AJ_SWOPE
ALIBATES
CTT_CROS
CTT_GRAY
OGALLALA
RAILHEAD
TESLA
TULECNYN
W_CW_345
WHIT_RVR
WINDMILL

## Slide 12: Statistics of Real Time RN LMPs
Mean difference = $0.08
Median = $0.00
Max difference = $59.72
Correlation between known Resource Nodes in the proposed hub is very strong, but weaker compared to existing Hubs. A better look would be to compare proposed Hub bus LMPs, but data is not readily available.
 | AEEC | BRISCOE | COTPLNS | GRANDVW1 | HRFDWIND | LHORN_N | MARIAH | MIAM1 | PH1 | PH2 | HB_NORTH | HB_WEST
AEEC | 1.00 |  |  |  |  |  |  |  |  |  |  | 
BRISCOE | 1.00 | 1.00 |  |  |  |  |  |  |  |  |  | 
COTPLNS | 1.00 | 1.00 | 1.00 |  |  |  |  |  |  |  |  | 
GRANDVW1 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  |  |  |  |  | 
HRFDWIND | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  |  |  |  | 
LHORN_N | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  |  |  | 
MARIAH | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  |  | 
MIAM1 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  | 
PH1_UNIT1_2 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  | 
PH2_U1_U2 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  | 
HB_NORTH | 0.95 | 0.95 | 0.94 | 0.95 | 0.95 | 0.95 | 0.94 | 0.95 | 0.95 | 0.95 | 1.00 | 
HB_WEST | 0.96 | 0.96 | 0.95 | 0.96 | 0.96 | 0.96 | 0.95 | 0.96 | 0.96 | 0.96 | 0.98 | 1.00

## Slide 13: The Abernathy Option
Several potential plans would tie the panhandle in to the rest of the system through Abernathy making it an intuitive candidate for a Hub Bus.
PREZ Study Report
LP&L Option 4OW
Sharyland South Plains
OGALLALA
ABERNATH

## Slide 14: Recommendation
ALIBATES
CTT_GRAY
CTT_CROS
OGALLALA
W_CW_345
ABERNATH
AJ_SWOPE
RAILHEAD
TULECNYN
TESLA
WINDMILL
WHIT_RVR
ABERNATH
AJ_SWOPE
ALIBATES
CTT_CROS
CTT_GRAY
OGALLALA
RAILHEAD
TESLA
TULECNYN
W_CW_345
WHIT_RVR
WINDMILL

## Slide 15: Risks
Panhandle interface shifts?
Significant Lubbock upgrade beyond plan 4OW?
Additional Load Transfer to ERCOT?

## Slide 16: Questions?
Brandon Whittle
www.megawattanalytics.com

## Slide 17: Raw Result – 30 Busses
ABERNATH
AEEC
AJ_SWOPE
ALIBATES
ALN_CRK
ASTRA
BRISCOE
COTPLNS
CTT_CROS
CTT_GRAY
GRANDVW1
HRFDWIND
LHORN_N
MARIAH
MIAM1
OGALLALA
PH1
PH2
RAILHEAD
ROUTE_66
SALTFORK
SPLAIN1
SPLAIN2
SSPURTWO
TESLA
TULECNYN
W_CW_345
WAKEWE
WHIT_RVR
WINDMILL

## Slide 18: Intuition? – 11 Busses, Debate!
AJ_SWOPE
ALIBATES
CTT_CROS
CTT_GRAY
OGALLALA
RAILHEAD
TESLA
TULECNYN
W_CW_345
WHIT_RVR
WINDMILL
ALIBATES
CTT_GRAY
CTT_CROS
OGALLALA
W_CW_345
AJ_SWOPE
RAILHEAD
TULECNYN
TESLA
WINDMILL
WHIT_RVR