## Slide 1
Base Point Deviation Charges for Energy Storage Resources
Magie Shanks
ERCOT
BESTF Meeting
10/18/2019

## Slide 2: Overview
NPRR963 introduces:
  The aggregation of the Generation Resource and the Controllable Load Resource for an energy storage resource into a group, Generation and Controllable Load Resource (GCLR) Group.
  Proposes a new methodology for calculating Energy Storage Resource Energy Deployment Performance (ESREDP) metric.
  Proposes a new methodology for calculating Base Point Deviation for the GCLR Group.

## Slide 3: Base Point Deviation Settlement
Current Base Point Deviation Settlement:
  The over/under performance of the energy storage resource is analyzed individually for the Generation Resource and the Controllable Load Resource, not as a group, per NP 6.6.5, Base Point Deviation Charge.
Proposed Base Point Deviation Settlement w/NPRR963:
  Energy storage resources will be aggregated in a Generation and Controllable Load Resource (GCLR) Group and the over/under performance will be analyzed as a group.
  New deviation tolerances for GCLR Group

## Slide 4: Example
Controllable Load Resource (CLR) receives a base point at 25 MW (charging)
Generation Resource (GR) at 0 MW
Both Receive simultaneous Reg-Up Instructions
  GR receives 10MW instruction
  CLR receives 13MW instruction
ESR provides full response by reducing consumption on CLR

## Slide 5: Example
Generation Resource (Under Generation) | 
AABP (BP + RegUp) = (0 +10) | 10MW
TWTG | 0MW
Tolerance: Min(MW, %): | 
MW Limit (AABP - 5MW) | 5MW
% Limit (AABP *0.95) | 9.5MW
Deviation (Tolerance-TWTG) | 5MW or 1.25MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $25
Controllable Load Resource (Under Consumption) | 
AABP (BP – RegUp) = (25-13) | 12MW
ATPC | 2MW
Tolerance: Min(MW, %): | 
MW Limit (AABP -2MW) | 10MW
% Limit (AABP *0.90) | 10.8MW
Deviation (Tolerance-ATPC) | 8MW or 2MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $40
GCLR Group | 
Net AABP = (10-12) | -2MW
Net Performance (TWTG-ATPC) | -2MW
Deviation | 0MW or 0MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $0
Current BPD Settlement
Proposed BPD Settlement
AABP = Adjusted Aggregated Base Point
ATPC = Average Telemetered Power Consumption
TWTG = Time Weighted Telemetered Generation
RTSPP = Real-Time Settlement Point Price
BPDAMT = Base Point Deviation Amount

## Slide 6: Deviation Tolerances
Generation Resource:
  Over and Under Generation is 5MW or 5%
Controllable Load Resource:
  Over Consumption:
    Carrying Ancillary Service (AS) is 2MW or 15%
    Not carrying AS is 2MW or 25%
  Under Consumption:
    Carrying AS is 2MW or 10%
    Not carrying AS is 2MW or 15%
GCLR Group:
  Over and Under Performance is 3MW or 3%

## Slide 7: Questions?

## Slide 8
Energy Storage Resource Energy Deployment Performance (ESREDP)
Luke Butler
ERCOT
BESTF Meeting
10/18/2019

## Slide 9: Why ESREDP?
Energy storage resources (ESR)* Actual vs Model (cont.)
  Our system does not recognize that ESR-GR/CLR are part of the same device.
  ESR-GR currently scored using Generation Resource Energy Deployment Performance (GREDP)
  ESR-CLR currently scored using Controllable Load Resource Energy Deployment Performance (CLREDP)
  In reality, an ESR is a single device and can only respond in one direction, i.e., ESRs can only consume or inject power at any given instant.
  Goal: Create a metric that captures performance of the ESR as a whole
*Energy storage resource (ESR) is not yet a defined ERCOT term.

## Slide 10: Example
Example 1
QSE holds 50 MW Regulation-Up Responsibility (RURS) on ESR
Telemetered RURS as 25 MW on ESR-GR and 25 MW on ESR-CLR
ESR-CLR Base-Point at 25 MW (charging)
ESR-GR at 0 MW
Both Receive simultaneous Reg-Up Instructions
ESR provides full response by reducing consumption on ESR-CLR

## Slide 11: Example
Chart: ESR-GR REG REQUEST
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR-GR REG REQUEST | 0 | 5 | 10 | 11.5 | 12 | 12.5 | 12 | 11.5 | 10 | 5 | 0
Chart: ESR-CLR REG REQUEST
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR-CLR REG REQUEST | 0 | 5 | 10 | 11.5 | 12 | 12.5 | 12 | 11.5 | 10 | 5 | 0
Chart: ESR REG REQUEST
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR REG REQUEST | 0 | 10 | 20 | 23 | 24 | 25 | 24 | 23 | 20 | 10 | 0

## Slide 12: Example
Chart: ESR-CLR RESPONSE
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR-CLR RESPONSE | 25 | 15 | 5 | 2 | 1 | 0 | 1 | 2 | 5 | 15 | 25
ESR-CLR BP | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
Chart: ESR-GR RESPONSE
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR-GR RESPONSE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ESR-GR BP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: ESR RESPONSE
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR RESPONSE | 0 | 10 | 20 | 23 | 24 | 25 | 24 | 23 | 20 | 10 | 0

## Slide 13: Example
Scoring* performance at the individual Resource level using GREDP/CLREDP metrics
Current protocol requirement must have a GREDP/CLREDP less than the greater of 8% or 8 MW  perfect performance gives score of 0% and 0 MW
GREDP (%) | GREDP (MW)
100 | 8.14
CLREDP (%) | CLREDP (MW)
48.25 | 8.14
*Assuming example is across a 5-min period
ATG = Average Telemetered Generation
ARI = Average Regulation Instruction
AEPFR = Average Estimated Primary Frequency Response
ABP = Average Base Point
ATPC = Average Telemetered Power Consumption
ARI = Average Regulation Instruction
AEPFR = Average Estimated Primary Frequency Response
ABP = Average Base Point

## Slide 14: GREDP/CLREDP vs ESREDP (%)
Combining scoring formulas to create an ESR net performance score

## Slide 15: GREDP/CLREDP vs ESREDP (MW)
)

## Slide 16: Example
Scoring* performance using ESREDP
ESREDP (%) | ESREDP (MW)
0 | 0
*Assuming example is across a 5-min period
)
)
)

## Slide 17: Example 2
Example 2
QSE holds 50 MW Regulation-Up Responsibility (RURS) on ESR
Telemetered RURS as 25 MW on ESR-GR and 25 MW on ESR-CLR
ESR-CLR Base-Point at 25 MW (charging)
ESR-GR at 0 MW
Both Receive simultaneous Reg-Up Instructions
ESR provides full response with a combination of reducing consumption on ESR-CLR and injecting with ESR-GR

## Slide 18: Example 2
Chart: GR REG REQUEST
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
GEN REG REQUEST | 0 | 5 | 12.5 | 12.5 | 15 | 15 | 15 | 12.5 | 12.5 | 5 | 0
Chart: CLR REG REQUEST
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
CLR REG REQUEST | 0 | 5 | 12.5 | 12.5 | 15 | 15 | 15 | 12.5 | 12.5 | 5 | 0
Chart: ESR REG REQUEST
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR REG REQUEST | 0 | 10 | 25 | 25 | 30 | 30 | 30 | 25 | 25 | 10 | 0

## Slide 19: Example 2
Chart: GR RESPONSE
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
GEN RESPONSE | 0 | 0 | 0 | 0 | 5 | 5 | 5 | 0 | 0 | 0 | 0
GR BP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: CLR RESPONSE
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
CLR RESPONSE | 25 | 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 25
CLR BP | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
Chart: ESR RESPONSE
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ESR RESPONSE | 0 | 10 | 25 | 25 | 30 | 30 | 30 | 25 | 25 | 10 | 0

## Slide 20: Example
Scoring* performance at the individual Resource level using GREDP/CLREDP metrics
Current protocol requirement must have a GREDP/CLREDP less than the greater of 8% or 8 MW  perfect performance gives score of 0% and 0 MW
GREDP (%) | GREDP (MW)
85.71 | 8.18
CLREDP (%) | CLREDP (MW)
52.94 | 8.18
*Assuming example is across a 5-min period

## Slide 21: Example 2
Scoring* performance using ESREDP
ESREDP (%) | ESREDP (MW)
0 | 0
*Assuming example is across a 5-min period
)
)

## Slide 22: ESREDP vs GREDP/CLREDP Criteria
GREDP and CLREDP:
  Must be less than the greater of X % or Y MW for 85% of the five-minute clock intervals in the month during which GREDP/CLREDP is calculated
    X and Y are currently set to 8% or 8 MW
ESREDP criteria uses new variables
  Must be less than the greater of V % or W MW for 85% of the five-minute clock intervals in the month during which ESREDP is calculated
    Proposing to initially set V and W both to 3

## Slide 23: Questions?