## Slide 1
ESRs and Updating EOCs Closer to Real-Time
David Maggio
October 18, 2019

## Slide 2: Acronyms
Average Incremental Energy Cost (AIEC)
Energy Offer Curve (EOC)
Energy Storage Resource (ESR)
Limited Duration Resource (LDR)
Nodal Protocol Revision Request (NPRR)
Real-Time Average Incremental Energy Cost (RTAIEC)
Security-Constrained Economic Dispatch (SCED)

## Slide 3: Recap on NPRR967 Discussions
The current window for submitting and updating EOCs for use in SCED closes at the end of the Adjustment Period (i.e., one hour prior to the beginning of the Operating Hour).
NPRR967, originally titled “Allow Limited Duration Resource Energy Offer Curve Updates Near Real-Time and Remove the 10 MW Limit”, was submitted on August 27, 2019 and proposed to broaden this window for LDRs.
  EOC updates allowed within the Operating Hour for LDRs.
  Requires that a valid EOC be in place in advance (submitted within the current window).
Comments have since been submitted by the sponsor striking this language, however this presentation follows from discussion on the NPRR.

## Slide 4: Potential Lower Cost Solution
An Impact Analysis has not been completed for the intra-hour approach proposed in the NPRR967, but there is some expectation of significant cost.
An alternative that would limit complexity and implementation timeline would be to change the window to end just prior to the beginning of the Operating Hour, adding an extra hour for updates.
  Allowing EOCs to be submitted one hour closer to Real-Time than today.
This proposal does not provide the same level of flexibility intended by NPRR967, but combined with the ability of LDRs to telemeter a status of “OFF” may provide the flexibility that LDRs are seeking.
This proposal does avoid some of the concerns raised regarding the effect of intra-hour EOC updates on indicative pricing.

## Slide 5: Considerations if Intra-hour EOC Submittals are Necessary
If the flexibility provided by the previous proposal is insufficient, ERCOT would like to raise the following ideas for discussion.
  Have the language around the timing of submittals be less specific (relative to NPRR967). More specific language may lead to complications for implementation.
  Allow for intra-hour submittals to be a separate submittal type. ERCOT believes this may help mitigate potential impacts to system performance.
  Fuel percentages are part of the existing EOC submittals. Allowing fuel percentages to be updated intra-hour has potential downstream impacts.

## Slide 6: Restricting to LDRs
LDR is not currently an attribute in the ERCOT systems.
This leaves two options for implementation, should the restriction to LDRs remain in place.
  Behavioral - No validation checks for the attribute within ERCOT systems.
  Systematic – Change systems and process to capture this attribute as part of Resource registration. Pass the LDR designation to downstream systems for performing validation.

## Slide 7: Note on NPRR971
ERCOT staff submitted NPRR971, Changing Energy Offer Curve Caps for Make-Whole Calculation Purposes and Replacing the Real-Time Average Incremental Energy Cost, on September 24, 2019.
Because the Settlement system uses EOCs to calculate RTAIEC, NPRRs that modify the timing of submission for EOCs or that modify the ERCOT creation or modification of submitted EOCs result in unintended Settlement system impacts.
  Section 6.5.7.3, Security Constrained Economic Dispatch
While NPRR971 does have a $60k to $90k Impact Analysis, replacing the RTAIEC should reduce the impact of future system changes for NPRRs like NPRR967.

## Slide 8: Questions