## Slide 1
Switching Plans & Conditional Contingency Definitions
Mario Alberto de la Garza
Network Modeling Maintenance Supervisor
10/15/2019

## Slide 2: Switching Plans & Conditional Contingency Definitions
Changes In Process
Contingency Stats As Of September 2019
Challenges
Switching Plans & Conditional Contingency Definitions Pilot Project
Switching Plans
How Would SWPs Be Maintained?
How Would SWPs Affect Contingencies?
Example
Pending Items
Long Term Goals
Benefits
Q/A

## Slide 3: Changes in Process
Prior to Model Maintenance Taking Over:
  One point of contact.
  Limited visibility to model changes.
Model Maintenance Taking Over:
  Multiple individuals involved.
  Increased visibility due to reviewing each NOMCR individually.

## Slide 4: Contingencies Stats as of September 2018
*This include future 2019 Manual Contingencies.

## Slide 5: Challenges
Increase in system changes.
  Multiple projects in the pipeline.
  Load growth.
Complex modeling solution to accommodate system changes.

## Slide 6: Switching Plans & Conditional Contingency Definitions Pilot Project
Goals:
  Efficient way to maintain “transitional” manual contingencies.
  Reduce amount of CAMRs.
  Improve situational awareness when a “transition” happens in real time.*
  Reduce amount of DPCs.*
Proof of Concept: Switching Plans & Conditional Contingency Definitions (aka CCDs)
* Long term goals.

## Slide 7: Switching Plans
What is a Switching Plan (SWPs)?
  A new modeling construct to track “transitional” (pseudo) switches (not an extension).
  Maintainable by TSPs directly.
  SWPs would be Validated by ERCOT.
Switch Action 1 - Open
Switch Action 1 - Close
SUBB
SUBA
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS (N.C.)
SWP1
Stage 1
Stage 2

## Slide 8: Switching Plans, Con’t
Switch Action 1 - Open
Switch Action 1 - Close
SWP1
Stage 1
Stage 2
Goal is to capture different stages of a project through the SWP.
  Stage 1 should be “current” configuration.
  Stage 2 should be “future” configuration.
SUBB
SUBA
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS (N.C.)

## Slide 9: How Would SWPs Be Maintained?
The idea is for TSPs to Maintain their own SWPs.
ERCOT would provide a “directory” in the model which SWPs can be modeled under.
SWPs would be associated to a specific ownership.
Since SWPs would be associated to certain devices, when deleting an associated device the TSP would need to update the SWP(s).

## Slide 10: How Would SWPs Affect Contingencies?
The Contingency Maintainer traces contingencies based of modeled statuses of breakers and switches.
SUBB
SUBA
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS (N.C.)
CTG ID: SAB138

## Slide 11: How Would SWPs Affect Contingencies? Con’t
When a SWP is associated to a disconnector, the Contingency Maintainer would re-trace the contingencies using the data provided in the SWP stages.
If a Contingency associated to a stage matches an existing contingency, it associates the existing contingency to the stage.
If a Contingency associated to a stage does not match an existing contingency, it creates a Conditional Contingency Definition (aka CCD) and associates the CCD to the stage.

## Slide 12: How Would SWPs Affect Contingencies? Con’t
Stage 1 Example.
SUBB
SUBA
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS (N.C.)*
CTG ID: SAB138
Switch Action 1 - Open
Switch Action 1 - Close
SWP1
Stage 1
Stage 2

## Slide 13: How Would SWPs Affect Contingencies? Con’t
Stage 2 Example.
SUBB
SUBA
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS (N.O.)*
CTG ID: CAC138
CTG ID: CCB138
Switch Action 1 - Open
Switch Action 1 - Close
SWP1
Stage 1
Stage 2

## Slide 14: Additional Example #1
Stage 1
SUBB
SUBA
Line: A_B_1
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS1 (N.C.)
PS2 (N.C.)
PS4 (N.O.)
PS3 (N.O.)
SWP2
Switch Action 1 - Close
Switch Action 2 - Close
Switch Action 3 - Open
Switch Action 4 - Open
Stage 1
Switch Action 1 - Open
Stage 2
Switch Action 2 - Open
Switch Action 3 - Close
Switch Action 4 - Close

## Slide 15: Additional Example #1, Con’t
Stage 2
SUBB
SUBA
Line: A_B_1
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS1 (N.C.)
PS2 (N.C.)
PS4 (N.O.)
PS3 (N.O.)
SWP2
Switch Action 1 - Close
Switch Action 2 - Close
Switch Action 3 - Open
Switch Action 4 - Open
Stage 1
Switch Action 1 - Open
Stage 2
Switch Action 2 - Open
Switch Action 3 - Close
Switch Action 4 - Close

## Slide 16: Additional Example #1, Con’t
Auto-traced Contingencies, same as Stage 1 Contingencies.
SUBB
SUBA
Line: A_B_1
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS1 (N.C.)
PS2 (N.C.)
PS4 (N.O.)
PS3 (N.O.)
CTG ID: SAB138
CTG ID: SAC138
CTG ID: SCB138
SWP2
Switch Action 1 - Close
Switch Action 2 - Close
Switch Action 3 - Open
Switch Action 4 - Open
Stage 1

## Slide 17: Additional Example #1, Con’t
Stage 2
SUBB
SUBA
Line: A_B_1
CB1
Line: A_C_1
Line: C_B_1
CB2
CB3
CB4
SUBC
PS1 (N.O.)
PS2 (N.O.)
PS4 (N.C.)
PS3 (N.C.)
SWP2
Switch Action 1 - Open
Stage 2
Switch Action 2 - Open
Switch Action 3 - Close
Switch Action 4 - Close
CTG ID: CAC138
CTG ID: CCB138
CTG ID: CAB138

## Slide 18: Pending Items
Testing Needed.
  Model Building.
  Contingency Maintainer.
  Other applications.
Double-Element Contingencies.

## Slide 19: Long Term Goals
All the items below are part of a long wish list of how SWPs and CCDs should be utilized.
Integrate SWPs into ERCOT’s EMS.
  Develop messaging schemes for notification.
  Pre-CA SWP contingency validation.
Utilize TSPs telemetry to trigger SWP’s stages in real time.
Utilize TSPs outages to trigger SWP’s stages in the long term horizon studies.

## Slide 20: Benefits
Improved process to manage contingencies.
Alleviates manual process.
Speeds up modeling process.
  Reduction of number of CAMRs.
  Reduction of number of Manual Contingencies.
Situational awareness improvements.*
Potential reduction of DPCs.*
*Based off long term goal.

## Slide 21: Questions?