## Slide 1
Key Topic 10
ESR - Study & Capacity Assumptions
BESTF Meeting
November 15, 2019

## Slide 2: Key Topic 10 ESR - Study & Capacity Assumptions
Define "Storage Peak Average Capacity Percentage" to be used in CDR for various batteries.
Outage Coordination Studies
Reliability Unit Commitment Studies (Nov 20th, TAC)
Operational Studies
Transmission Planning Studies

## Slide 3: Storage Peak Average Capacity Percentage for CDR
Currently assuming 0% capacity contribution from ESRs over peak
Similarly to PVGRs, ERCOT proposes to set a threshold of X MW capacity of 4-hour ESRs (KTC-10)
Peak Average Capacity Percentage methodology will be developed at SAWG and implemented once this threshold is reached by operational projects (KTC-10)
Factors to be considered in the methodology: duration or maximum SoC compared to duration of ERCOT peak load, intended use (AS, energy, or both)
Information about ESR duration (h) and/or maximum State of Charge (MWh) along with intended use (AS, energy, or both) for planned and existing resources will be requested via RIOO-IS (KTC-10)

## Slide 4: Outage Coordination Studies
Outage coordination studies currently do not include ESR
ESRs are not expected to have sufficient duration, where planned outages contingent on ESR capacity being available would be approved
This approach may need to be revised later when significant amount of ESR capacity is installed

## Slide 5: Operations Studies
Generic Transmission Constraint Limit study uses historical generation patterns as input
Next Day Study (for next day peak operation) uses COPs available at the time of DRUC run
GAP Study uses COPs available at HRUC runs
Currently the ESR are considered “offline” in the Operations Studies
ERCOT plans to provide guidance on COP submittal that will ensure COPs are better aligned with ERCOT’s expectations

## Slide 6: Transmission Planning Studies
Currently the ESR are considered “offline” in the Transmission Planning Studies
ERCOT will work with RPG and PLWG to develop appropriate assumptions for Transmission Planning Studies
Going forward, ERCOT will review the assumptions as necessary based on operational experience and ESR project growth.