## Slide 1
KP-7: Align Base-Point Deviation Settlement with GREDP/CLREDP Changes
Magie Shanks
ERCOT
RTCTF Meeting
12/03/2019

## Slide 2: Overview
Changes to Base Point Deviation (BPD) charge calculations that align with changes to GREDP/CLREDP.
KP-7: Generation Resource Energy Deployment Performance (GREDP) and Controllable Load Resource Energy Deployment Performance (CLREDP) calculations will updated to account changes made to deployments instructions from ERCOT. The “ABP” and “ARI” components of the GREDP and CLREDP calculations will be replaced with an Average Set Point (ASP) component, where ASP is equal to the time-weighted average of the Updated Desired Set Point (UDSP), which is sum of a linearly ramped Base Point (Base Ramp) and Regulation Service instruction that the Resource should have produced during a five-minute clock interval.

## Slide 3: BPD Settlement Input
Current Aggregate Adjusted Base Point (AABP):
  AABP = AVGBP + AVGREG
Proposed Aggregate Adjusted Base Point (AABP):
  AABP = ASP
AVGBP = Average Base Point
AVGREG = Average Regulation Instruction
ASP = Average Set Point

## Slide 4: Proposed Principle Concept
The Aggregate Adjusted Base Point (AABP) calculation used in the Base Point Deviation (BPD) Settlement will replace the sum of the Average Base Point (AVGBP) and the Average Regulation Instruction (AVGREG) with the Average Set Point (ASP) component.

## Slide 5: Questions?