## Slide 1
Southern Cross Transmission Directives
Directive #3 : Ramp rate
Proposed Whitepaper Concepts
January 2020, PDCWG
ERCOT Staff

## Slide 2: Directive #3
Upon the interconnection of Southern Cross Transmission DC Tie, there is a potential of up to a 4100 MW change in the DC tie’s schedule (based on the projected maximum import/export capability of the tie).
In order to determine whether ramp rate restrictions should be imposed on the DC tie, ERCOT and PDCWG evaluated;
  the impact to ERCOT’s net load variability due to a DC tie ramp of this magnitude, and
  the impact on ERCOT’s ability to recover from frequency events such as Reportable Balancing Contingency Events during the DC Tie ramps.
  Existing process for managing DC Tie schedules
ERCOT shall determine what ramp rate restrictions, if any, will be necessary to accommodate the interconnection of the Southern Cross DC tie and shall implement those restrictions and shall certify to the Commission when it has completed these actions.

## Slide 3: Recap of Directive #3 Discussions at PDCWG
ERCOT introduced Southern Cross Directive #3 at the April 2019 PDCWG meeting. Directive_3_Discussion_Points_v3.docx
  At the April 2019 PDCWG meeting, stakeholders requested ERCOT to provide high level overview of how the DC Ties are managed by Control Room today.
  Stakeholders also requested additional data related to usage of regulation during the DC tie ramps as well as historical net load ramp data.
At the June 2019 PDCWG meeting ERCOT presented both the items requested by the stakeholders.
  ERCOT_DC_Tie_Procedure.pptx
The August 2019 PDCWG meeting discussed potential approaches that may be utilized to manage DC Tie Ramps and if any specific restrictions were needed for Southern Cross DC Tie.
    SCT_Directive_3_Rec_PDCWG_Aug2019_v2.pptx
    Follow up with a draft recommendation based on the group’s discussion.
The October 2019 & December 2019 PDCWG meetings discussed ERCOT’s proposed recommendation of additional protocol language management of DC Tie Schedules due to ramp limitations.

## Slide 4: Proposed Determination
Determination: ERCOT will need to impose restrictions on DC Tie ramp rates when ERCOT determines that system conditions near or in Real-Time cannot accommodate the DC Ties’ scheduled ramp. Although ERCOT is required by NERC Reliability Standards to curtail DC Tie Schedules that cannot be accommodated, Nodal Protocol Revision Request ### has revised the Protocols to explicitly address ERCOT’s management of DC Tie Schedules due to ramp limitations.
Directive #3 – Ramp Rate Restrictions | ERCOT shall determine what ramp rate restrictions, if any, will be necessary to accommodate the interconnection of the Southern Cross DC tie and shall implement those restrictions and shall certify to the Commission when it has completed these actions.

## Slide 5: Technical Reasons for Determination
The interconnection of the SCT DC Tie brings a potential for a 4100 MW change in DC Tie Schedules.
NERC Reliability Standard INT-006-4 R1 requires ERCOT to reject or curtail a DC Tie Schedule that ERCOT does not expect to be capable of supporting either in magnitude or ramp.
Although the existing DC Ties in ERCOT typically ramp over 10 minutes from one hour to the next, ERCOT has the ability to either extend the duration of the ramp or de-rate the associated DC Tie Schedule in the event of an identified ramp limitation.
The ERCOT Protocols explicitly authorize ERCOT to take action to address physical capacity limitations and transmission security concerns but do not explicitly address the treatment of insufficient ramp capability due to schedules. The Protocols should be modified to clearly reflect how this insufficient ramp capability scenario will be handled, including by taking action to curtail DC Tie Schedules, in keeping with ERCOT’s responsibilities under the NERC Reliability Standards.
In the scenario where a tag may be rejected due to real time insufficient ramp capability, ERCOT may request for the tag to be resubmitted with a different ramp duration if there is sufficient time.
ERCOT also conducted an analysis of the usage of regulation during current DC Tie ramps, for ERCOT’s net load variability impact due to a DC Tie ramp of this magnitude, and for the impact on ERCOT’s ability to recover from frequency events such as Reportable Contingency Events during DC Tie Ramps. These should be considered regardless of the SCT directives due to the impacts associated with the current DC Ties.