## Slide 1
ORDC and RTRDPA Pricing Outcomes During August 2019 EEA Events
Aaron Townsend
WMWG
January 27, 2020

## Slide 2: Introduction
Stakeholders requested a review of the ORDC and Reliability Deployment Price Adder outcomes related to the reliability actions taken by ERCOT on August 13 and August 15, 2019

## Slide 3: Components of RTOLCAP for ORDC Adder
RTOLCAP = RTOLHSL – RTBP + RTCLRCAP + RTNCLRCAP – RTOLNSRS – RTPBPC
  RTOLHSL: Online Generator HSL
  RTBP: System Total SCED Base Points
  RTCLRCAP: Controllable Load Resource Capacity
  RTNCLRCAP: Non-Controllable Load Resource Capacity
  RTOLNSRS: Total Online Generator Non-Spin
  RTBPC: Power Balance Under-generation MW
Excludes Resources that are:
  Nuclear
  Telemetered MW less than 95% of telemetered LSL
  Status of STARTUP, SHUTDOWN, ONTEST, or ONRUC
OBDRR009 will subtract any ERCOT-directed DC tie net flow change from the RTOLCAP

## Slide 4: Real-Time Deployment Price Adder (RTORDPA)
The Reliability Deployment Price Adder is triggered by the following:
  RUC-committed Resources, unless Opted Out of RUC Settlement
  RMR Resources coming online to prevent an emergency condition
  Load Resources deployed by ERCOT other than Controllable Load Resources
  Deployed Emergency Response Service (ERS)
  Net ERCOT-directed DC Tie imports during an EEA
    NPRR904 will expand to include net ERCOT-directed changes in DC tie flows not during EEA—see NPRR904 for details
  Block Load Transfers (BLTs) delivering energy to ERCOT during an EEA or delivering energy from ERCOT to another power pool to address emergency conditions in the receiving grid

## Slide 5: Real-Time Deployment Price Adder (RTORDPA)
Modifications in Pricing Run are:
  ONRUC lower limits relaxed to zero
  Most other Resources’ limits relaxed to 60-minute ramp limit
    NPRR904 changes this to relax only the limits that were not binding in the dispatch run
  Additions to GTBD:
    ERCOT-deployed non-Controllable Load Resources
    ERS deployment contracted amounts (during deployment) or ramped recovery amounts (during recovery period)
    ERCOT-directed DC tie net imports during EEA
      NPRR904 will expand to include net ERCOT-directed changes in DC tie flows not during EEA—see NPRR904 for details
    Net Block Load Transfers during EEA

## Slide 6: August 13 Reliability Deployments
EEA1 declared at 15:10
ERS deployment
  At 15:18, ERS-10 (93 MW) and ERS-30 (833 MW) were deployed
  At 15:56, ERS-10 recall instruction was issued
  At 16:02, additional ERS-30 (0.1 MW) amount of was deployed
    Additional capacity contracted for Time Period 4
  At 16:14, ERS 30-minute recall instruction was issued
No DC tie emergency imports
RUC instructions
  At approximately 16:40, RUC VDI instructions were issued to five Hydro Resources (totaling 90 MW) to stay online for the remainder of delivery hour 17
  EEA1 canceled at 17:00

## Slide 7: August 13 Timeline and Prices
Chart: Reserves (MW)
Instructed RUC HSL | 0 | 92.57 | 92.57 | 92.57 | 92.57 | 0
15:18
ERS-10 (93 MW) and
ERS-30 (833 MW) deployed
16:14
ERS-30 recalled
System Lambda
RTOLCAP
PRC
System Lambda+
RTORPA+
RTORDPA
System Lambda+
RTORPA
RUC Instruction
17:04
EEA1 canceled
15:56
ERS-10 recalled
15:10
EEA1 declared

## Slide 8: August 13 ERS Addition to GTBD in the Reliability Deployment Pricing Run
Chart: Addition to GTBD (MW)
8/13 15:25
First non-zero RTORDPA SCED Interval
8/14 2:15
Last non-zero RTORDPA SCED Interval

## Slide 9: August 15 Reliability Deployments
EEA1 declared at 15:05
ERS deployment
  At 15:11, ERS-30 amount of 833.29 MW was deployed
  At 16:02, additional ERS 30-minute amount of 0.1 MW was deployed
    Additional capacity contracted for Time Period 4
  At 16:54, ERS-30 recall instruction was issued
DC Tie emergency import
  At 15:30, VDI instruction for additional 60 MW from DC Railroad was issued
  At 17:05, canceled VDI
RUC instructions
  At 15:53, RUC VDI instructions were issued to 2 Hydro Resources (totaling 48 MW) to stay online for the remainder of HE16 and also for HE17
EEA1 canceled at 17:05

## Slide 10: August 15 Timeline and Prices
Chart: Reserves (MW)
Instructed RUC HSL | 0 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 48.96 | 0
DC Tie Import | 0 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 0
15:11
ERS-30 (833 MW) deployed
System Lambda+
RTORPA
System Lambda
PRC
RTOLCAP
System Lambda+
RTORPA+
RTORDPA
RUC Instruction
DC Tie Import
17:05
EEA1 canceled
16:54
ERS-30 recalled
15:05
EEA1 declared

## Slide 11: August 15 ERS and DC Tie Additions to GTBD in the Reliability Deployment Pricing Run
Chart: Addition to GTBD (MW)
8/15 15:15
First non-zero RTORDPA SCED Interval
8/16 2:50
Last non-zero RTORDPA SCED Interval