## Slide 1
Settlement of ESRs During a Market Suspension and Restart
Ino González
ERCOT
BESTFORCE
May 21, 2020

## Slide 2: Market Suspension Triggering Event
A Market Suspension triggering event may result in the suspension and restart of market activities, including but not limited to:
Day-Ahead Market (DAM) activities;
Real-Time Market (RTM) activities;
Congestion Revenue Right (CRR) Auctions;
Market credit activities;
Retail market activities;
Network Operations Model updates;
Market reporting activities; and
Other impacted ERCOT operations and activities.

## Slide 3: Market Suspension Make-Whole Payment Principles
NPRR850, Market Suspension and Restart
QSEs representing Resources that support restoration of the ERCOT Transmission Grid shall be made whole to their costs as described in Section 25.5, Market Suspension and Market Restart Settlement.
Startup costs and operating costs incurred during a Market Suspension shall be uplifted on a Load Ratio Share (LRS) basis after Market Restart.

## Slide 4: Market Suspension Make-Whole Payment
Make-Whole Payment = (-1)* (Start-Up Cost + Operating Costs)
Where,
Start-Up Cost = Fuel Costs S + O&M S
Operating Costs = Fuel Costs Op. + O&M Op.
And,
S – start
Op - Operating

## Slide 5: Energy Storage Resources Compensation Principles
ESRs will be eligible for consideration to recover the following costs:
  Electricity charging costs that occurred before the Market Suspension
  Variable O&M costs that occurred during the Market Suspension period.
    $0.3/MWh1,2, or
    Actual O&M value incurred3
ESRs will not be paid a price for generation that occurred during the Market Suspension period.
ESRs will not be charged a price for consumption that occurred during the Market Suspension period.
1 Mongird et al. (July 2019). Page 8. Energy Storage Technology and Cost Characterization report. Hydro Wires. U.S. Department of Energy. https://www.energy.gov/sites/prod/files/2019/07/f65/Storage%20Cost%20and%20Performance%20Characterization%20Report_Final.pdf
2 Aquino et al. (Nov 29, 2017). Page 9. Battery Energy Storage Assessment. Platte River Power Authority.
https://www.prpa.org/wp-content/uploads/2017/10/HDR-Battery-Energy-Storage-Assessment.pdf
3 QSE may submit actual O&M costs after a Market Restart

## Slide 6: Energy Storage Resources Compensation Principles
If the ESR SOC1 at the end of the Market Suspension is less than the SOC at the beginning of the period, the ESR will be compensated for the following costs by submitting data within 5 months of the Market Restart with the following information:
  Electricity costs incurred by the ESR to charge the battery prior to a Market Suspension
  MWh difference discharged from the ESR
Charging related costs will be compensated on the Resource’s most recent MWh consumption prior to the Market Suspension.
1 soc – state of charge

## Slide 7: Energy Storage Resources Compensation Example
Data:
Market Suspension Start - September 1
Market Restart – September 5
ESR size - 10MW
SOC Sep 1 - 10MWh
SOC Sep 5 - 3MWh
MWs dispatched during market suspension
  20MWh
O&M - $0.3/MWh
ESR Load – 7MWh (MEBR+MEBL)1
Aux load – 1 MWh (if not included in MEBR)
1 measured as metered load as defined in NPRR986, BESTF-2 Energy Storage Resource Energy Offer Curves, Pricing, Dispatch, and Mitigation
Compensation:
Electricity charging costs (prior to Market Restart)
August 20:
ESR Load: 4 MWh @ $50 = $200
Aux Load: 0.5 MWh @ $50 = $25
August 15:
ESR Load: 3 MWh @ $100 = $300
Aux Load: 0.5 MWh @ $100 = $50
O&M costs (during Market Suspension)
20MWh * $0.3 = $6

## Slide 8: Energy Storage Resources Cost Uplift Principles
Costs incurred by the ESR prior and during the Market Suspension Period (e.g., load and O&M charges) shall be uplifted as follows:
  Allocated to the LRS that occurred during the suspension period on a daily load ratio share basis1.
Metered load to charge the ESR (MEBL + MEBR) will not be allocated Market Suspension Make Whole costs.
1 Similarly to the allocation of operating costs from other generators

## Slide 9: DC-Coupled Resources Compensation Principles
DC-Coupled Resources that discharge and/or charge during the Market Suspension period will be eligible for compensation for variable O&M incurred at:
  Standard O&M value as defined in the Protocols ($4.40/MWh1), or
  Actual O&M value incurred2
Just like other ESRs, DC-Coupled Resources:
  Will not be paid a price for generation that occurred during the Market Suspension period.
  Will not be charged a price for consumption that occurred during the Market Suspension period.
1 See Variable O&M costs for renewable Resources per 5.6.1 Verifiable Costs, paragraph (6), Table (c)
2 QSE may submit actual O&M costs after a Market Restart