## Slide 1
ERCOT Response to Market Questions on Issue #18
AS Demand Curves in context of current policy
ERCOT Staff
RTCBTF
June 14, 2024

## Slide 2: ERCOT responses to Issues 18
At prior RTCBTF meetings there have been questions and/or concerns about how the current policy and shape of AS Demand Curves may or may not affect ERCOT Operations in a negative manner.
ERCOT offers initial feedback on three themes of concerns:
  Certain product-priority in scarcity
  Risk that curtailed IRR will consume Ancillary Services stack
  Is the ORDC curve is aligned with operational needs?

## Slide 3: ERCOT responses to Issues 18
Certain product-priority in scarcity
  It sounds like that the question here is “Is ERCOT okay with any ECRS being awarded when in the system is in EEA or getting close? Or do we want the awards to focus more exclusively on Reg and RRS?”
  ERCOT Operations agrees that during scarcity conditions it is preferred for SCED to award reserves like RRS and Regulation.
  Further ERCOT Operations doesn’t necessarily consider it to be a serious flaw if SCED were to award other AS like ECRS.
  It’s also worth noting that, while not guaranteed, it’s feasible and maybe likely that headroom freed up through ECRS awards is frequency responsive and would be contributing to PRC.
  ERCOT Operations thinks it is worthwhile to study this particular scenario that has been raised using the RTC simulation tool that ERCOT Market Operations is developing to see if the outcomes make sense and align with current pricing policy.

## Slide 4: ERCOT responses to Issues 18
Risk that curtailed IRR will consume Ancillary Services stack
  ERCOT notes that under the RTC protocols that have currently been approved, the IRRs are able to qualify to provide AS and the IRR capability that is offered to provide AS is subject to duration requirements of the product.
  ERCOT Operations doesn’t necessarily see a flaw with some AS being provided by IRRs, although it will be important that COP and telemetered AS capability being provided by the QSEs is accurate.
  The question of whether IRRs should be completely precluded from providing AS is a policy discussion more than a current operational concern and that likely falls outside the purview of RTCBTF.

## Slide 5: ERCOT responses to Issues 18
Is the ORDC curve is aligned with operational needs?
  It sounds like that the question here is whether the current ORDC will lead to sufficient self-commitments?
  ERCOT Operations agrees that this is an important question.
  ERCOT thinks that RTC simulation tool that ERCOT Market Operations is developing can be used to build simulations operating condition to gauge if market pricing outcomes during a variety of scarcity/operating situations will be sufficient to incent Market response and maintain operating margins necessary to operate reliably.