## Slide 1
Nodal Operating Guide Revision Request (NOGRR) 245, Inverter-Based Resource (IBR) Ride-Through Requirements
ERCOT Update
August 8, 2024

## Slide 2: Disclaimer
If any part of this presentation differs from the contents of NOGRR 245, the NOGRR prevails
This presentation is based on a draft and NOGRR 245 may be changed before ERCOT presents official comments

## Slide 3: NOGRR 245 Background
ERCOT filed original NOGRR on 1/11/23 based on:
  Recommendations from NERC in connection with ERCOT Region events in which IBRs failed to ride-through system disturbances
  NERC recommendations to industry
  IBRTF recommendations
  IEEE 2800 approval
On 2/8/23, ROS tabled NOGRR and referred the issue to OWG, DWG, IBRTF
  MPs/ERCOT filed comments between 2/16/23 and 9/13/23
On 9/14/23, ROS granted NOGRR urgent status and recommended approval as amended by the 9/13/23 NextEra comments and as revised by ROS
  MPs/ERCOT filed comments between 9/22/23 and 9/25/23
On 9/27/23, TAC tabled NOGRR
  MPs/ERCOT filed comments between 9/29/23 and 3/26/24

## Slide 4: NOGRR 245 Background (cont’d)
On 3/27/24, TAC voted to recommend NOGRR as recommended by ROS on 9/14/23 as amended by Joint Commenters’ comments and as revised by TAC
  MPs/ERCOT filed comments on 4/15/24
On 4/23/24, ERCOT Board remanded NOGRR to TAC
On 5/22/24, TAC tabled NOGRR
  MPs/ERCOT filed comments between 6/5/24 and 6/6/24
On 6/7/24, TAC voted to recommend approval of NOGRR as recommended by TAC in its 3/27/24 report as amended by the 6/5/24 ERCOT comments as revised by TAC
  MPs/ERCOT filed comments between 6/10/24 and 6/16/24

## Slide 5: NOGRR 245 Update
Prior to the 6/17/24 Reliability & Markets (R&M) Committee Meeting:
  Joint Commenters’ comments opposed TAC-recommended version
  Joint Commenters informed ERCOT of intent to appeal TAC-recommended version if ERCOT Board of Directors sent it to PUC
  Appeal would delay the benefits to system reliability of NOGRR245
On 6/16/24, ERCOT filed comments requesting R&M Committee recommend tabling NOGRR until a Special Meeting or regularly-scheduled August meeting to allow bifurcating the exemptions process and allow other clarifications to accommodate Joint Commenters
On 6/18/24, ERCOT Board tabled NOGRR 245 based on ERCOT comments

## Slide 6: NOGRR 245 Update
ERCOT worked with Joint Commenters on revisions to:
  Retain some near-term benefits of TAC-recommended NOGRR 245
  Remove the details and criteria of exemption process to subsequent NOGRR (to achieve bifurcation)
  Provide clarifications, remove redundancy and correct errors
ERCOT comments identify specific reason for each change to TAC-recommended version:
  Clarification or to obtain JC agreement
  Bifurcation of exemption criteria
  Correction
  Duplication/Redundancy
ERCOT will recommend the ERCOT Board designate subsequent NOGRR as Board Priority Revision Request with timeline to become effective by 4/1/25 to coincide with deadline for submitting exemption requests

## Slide 7: Changes to TAC-Recommended NOGRR 245
1. Clarification/JC Concern
§ 2.6.2.1(4); § 2.9.1.1(4); § 2.9.1.2(4) Based on JC request to make it clear requirement does not apply when output reductions result from wind speed or solar irradiance changes (taken from NERC PRC-030)
§ 2.6.2.1(5); § 2.9.1.1(5); § 2.9.1.2(5) JC concern about phrase “power output”
§ 2.6.2.1(6) (i) ERCOT must know date Resource maximized ride-through capability (for modelling); (ii) defines how to determine if Resource “maximized” ride-through capability to equipment limits; and (iii) adds element of “Good Utility Practice” per JC request
§ 2.9.1(5) Date by which modifications must be completed
§ 2.9.1(8) ERCOT must know when Resource maximized its ride-through capability (for modelling – see, § 2.6.2.1(6), above)
§ 2.9.1.1(7) (renumbered); § 2.9.1.2(7) To include fault and recovery period
§ 2.11 Adds 3 sub-sections to clarify RE must tell ERCOT if it considers a Resource "already maximized" or completes maximization and Resource must comply with ride-through requirements from 5/1/24 until maximized

## Slide 8: Changes to TAC-Recommended NOGRR 245
§ 2.9.1.2(9) For when Resource cannot meet 12/31/25 deadline to maximize
§ 2.11.1(1) (i) Enumerates info RE must include in IFRTCR; (ii) removes requirements JCs found objectionable; (iii) per JC request, allows RE to explain why it could not get OEM/consultant to verify limitations; (iv) RE cannot get exemption/extension if it does not timely file IFRTCR
§ 2.11.2(1) Same as § 2.11.1(1) but for IVRTCR
§ 2.12.1(10) (renumbered) Until exemption/extension/appeal is final, Resource must meet greater of maximized ride-through capability or ride-through requirements from 5/1/24
§ 2.12.1(11) (renumbered) ERCOT will not report Resource to ERM based on IFRTCR/IVRTCR so long as Resource meets certain requirements
§ 2.12.1(12) (renumbered) Info submitted is Protected Information
§ 2.12.1.1(2) RE requesting exemption must timely submit IFRTCR/IVRTCR and removes data requirements moved to IFRTCR/IVRTCR sections
§ 2.12.1.2(1) RE must submit extension requests by 4/1/25

## Slide 9: Changes to TAC-Recommended NOGRR 245
2. Bifurcation
§ 2.6.2.1(7) Resources will submit IFRTCR and request exemptions by 4/1/25 but criteria for exemptions to be established in new NOGRR
§ 2.12.1(1) Confirms existing facilities not meeting ride-through requirements must request extension/exemption by 4/1/25 and criteria for exemption will be determined in subsequent NOGRR
§ 2.12.1(2) Exemption requests may only be supplemented w/ additional info under process established in subsequent NOGRR and no new exemption requests after 4/1/25
§ 2.12.1.3 Removed “exemption” from title because it now applies to only extension requests
§ 2.12.1.3(3), (4) and (5) Removed references to exemptions (to be addressed by subsequent NOGRR)
§ 2.12.1.4(6), (7) Removed references to exemptions (to be addressed in subsequent NOGRR)

## Slide 10: Changes to TAC-Recommended NOGRR 245
3. Corrections
§ 2.9.1.1(1) Typographical errors in formulae in Tables A & B
§ 2.9.1.1(8) (renumbered) Corrects paragraph numbers due to deletion of original section 2.9.1.1(7) and REs must complete maximization by 12/31/25
§ 2.9.1.2(7) Number changed to (7)
§ 2.12.1(1) Corrects section references
§ 2.12.1.4 Title removed and sub-sections renumbered as part of § 2.12.1.3

## Slide 11: Changes to TAC-Recommended NOGRR 245
4. Redundancy
§ 2.9.1.1(1) Removed Table C (same requirements as IEEE 2800-2022 § 7.2.3)
§ 2.9.1.1(7) Requirement already covered in § 7.2.2.4 of IEEE 2800-2022
§ 2.9.1.1(8); § 2.9.1.2(7) Remove sentence b/c ¶(1) already requires ride-through during disturbances regardless of phase angle or rate-of-change-of-frequency
§ 2.9.1.1(9) and 2.12.1.2(5) (renumbered) Due to removal of Table C (described above)
§ 2.12.1(3), (4); § 2.12.1.2(5) Deleted because requirements are captured in revised language for IFRTCRs/IVRTCRs and to address language JCs found objectionable
§ 2.12.1(9) (renumbered) Corrects section due to modification

## Slide 12: Recap of Change Types
Category 1 - Clarification or JC concern |  |  | 
2.6.2.1(4) 2.6.2.1(5) 2.6.2.1(6) 2.9.1(5) 2.9.1(8) | 2.9.1.1(4) 2.9.1.1(5) 2.9.1.1(7) 2.9.1.2(4) 2.9.1.2(5) | 2.9.1.2(7) 2.9.1.2(9) 2.11 2.11.1(1) 2.11.2(1) | 2.12.1(10) 2.12.1(11) 2.12.1(12) 2.12.1.1(2) 2.12.1.2(1)
Category 2 – Bifurcation of exemption criteria |  |  | 
2.6.2.1(7) 2.12.1(1) 2.12.1(2) | 2.12.1.3 2.12.1.3(3) | 2.12.1.3(4) 2.12.1.3 | 2.12.1.4(6) 2.12.1.4(7)
Category 3 - Corrections |  |  | 
2.9.1.1(1) 2.9.1.1(8) | 2.9.1.2(7) | 2.12.1(1) | 2.12.1.4
Category 4 – Duplication/Redundancy |  |  | 
2.9.1.1(1) 2.9.1.1(7) 2.9.1.1(8) | 2.9.1.1(9) 2.9.1.2(7) | 2.12.1(3) 2.12.1(4) | 2.12.1(9) 2.12.1.2(5)

## Slide 13: Next Steps
On 8/19/24, R&M Committee to discuss
  ERCOT will present results of Request for Information associated with Market Notices M-C050124-01 and M-C050124-02 to maximize IBR and WGR ride-through capability
On 8/20/24, ERCOT Board to consider NOGRR245
After/if PUCT approval of NOGRR 245, ERCOT will file new NOGRR to develop exemption criteria as soon as possible

## Slide 14
Pre-8/1/24 SGIA IBR/Type 1/Type 2 WGRs

## Slide 15: New Process – Pre-8/1/24 IBR/Type 1/Type 2 WGR
Frequency Ride-Through
By 12/31/25 (or sync date), maximize software, firmware, settings, parameterization (SFSP) (incl. memory) to meet or exceed § 2.6.2.1(1)-(5) and IEEE 2800 per § 2.9.1(8) and inform ERCOT when maximized [§ 2.6.2.1(6); § 2.9.1(8)]
If cannot by 12/31/25, submit IFRTCR by 4/1/24 and comply with requirements in effect on 5/1/24 until maximized [§ 2.6.2.1(7)]
Resources that have not implemented modifications to meet §2.6.2.1(1)-(5) must temporarily meet § 2.6.2.1.1(2)-(3) [§ 2.6.2.1.1(1)]
  If such Resource cannot remain reliably connected it must:
    Provide ERCOT accurate model reflecting field settings
    Comply w/ FRT requirements in effect on 5/1/24
    Inform ERCOT when maximized
On performance failure: take actions in §2.13

## Slide 16: New Process – Pre-8/1/24 IBR/Type 1/Type 2 WGR
Frequency Ride-Through (cont’d)
IFRTCR must contain: [§2.11.1(1)]
Resource Entity DUNS # | SFSP modifications done to maximize
Site Name | Changes beyond SFSP (if any)
Unit Name(s) | Expected post-modification limitation(s)
NOG Section(s) Resource cannot meet | Implementation schedule
Current FRT capability | Model of expected performance with limitations identified
Known FRT limitations compared to requirements in § 2.6.2.1(1) - (5) | Description of limitation that cannot be modeled
Detailed description of limitation(s) preventing Resource from meeting ride-through requirement(s) | 
NOTE: ERCOT will not use IVRTCR for referral to ERM so long as Resource meets greater of: (i) maximized capability or (ii) requirements in effect 5/1/24 [§2.12.1(11)]

## Slide 17: New Process – Pre-8/1/24 IBR/Type 1/Type 2 WGR
Voltage Ride-Through
Meet or exceed § 2.9.1.2(1)-(7) by 12/31/25 or COD (whichever is later) [§ 2.9(1)(b); § 2.9.1.2(8)]
If cannot:
  By 4/1/25, submit IVRTCR* and request extension [§ 2.9.1.2(9)]
  If cannot meet § 2.9.1.2(1)-(7) even w/ extension, submit IVRTCR and comply w/ requirements in effect 5/1/24 until VRT maximized [§ 2.9.1.2(9)]
    NOTE: IBR/Type 1/2 WGR that modifies to meet § 2.9.1.2 before 1/1/28 need not meet IEEE 2800 [§ 2.9.1(4)]
    NOTE: Type 1/2 WGR not required to meet IEEE 2800 but must meet § 2.9.1.2 [§ 2.9.1(7)]
  Comply w/ requiremets in effect on 5/1/24 during pendency of extension/exemption/ appeal
* Same data as IFRTCR and ERCOT will not use IVRTCR for referral to ERM so long as Resource meets greater of: (i) maximized capability or (ii) requirements in effect on 5/1/24 [§2.12.1(11)]

## Slide 18: New Process – Pre-8/1/24 IBR/Type 1/Type 2 WGR
Frequency or Voltage
During exemption/extension/appeal process, Resource must meet greater of: (i) maximized capability or (ii) requirements in effect 5/1/24 [§2.12.1(10)]
If Exemption granted:
  Maximized capability = performance criteria unit exemption/extension ends [§2.12.1(4)]
If new SFSP modifications become available, w/n 90 days, submit plan to implement and implement w/n 180 days of approval of plan [§2.12.1(7)]
If RE believes Resource has already maximized ride-through capabilities or will maximize w/ SFSP changes before 12/31/25, provide ERCOT an accurate model showing field settings [§ 2.11(1)]
Until Resource completes maximization per §§ 2.6.2.1, 2.9.1, 2.9.1.1 or 2.9.1.2, it must meet requirements in effect on 5/1/24 [§ 2.11(2)]
When maximization work complete, notify ERCOT [§ 2.11(3)]
On performance failure, follow § 2.13

## Slide 19
Post-8/1/24 SGIA or “Re-powered” IBR/Type 1/2 WGRs

## Slide 20: New Process – Post-8/1/24 or “Re-powered” IBR/Type 1/2 WGR
Frequency Ride-Through
Meet/exceed § 2.6.2.1(1)-(5) and IEEE 2800 [§ 2.6.2.1(1) and § 2.9.1(8)]
New IBRs synchronized after 12/31/25 must inform ERCOT of date of maximization [§ 2.6.2.1(6)]
On Performance Failure, follow § 2.13

## Slide 21: New Process – Post-8/1/24 IBR or “Re-powered” IBR/Type 1/2 WGR
Voltage Ride-Through
Maximize to meet/exceed §2.9.1.1(1)-(8) (Preferred Requirements) [§ 2.9.1(1)(a)] and IEEE 2800-2022, Sections 5, 7, 9 at POIB [§2.9.1(2), (3), (8)]
If cannot do so by synchronization date:
  Request temporary extension (extensions cannot go past 12/31/28) [§ 2.9.1(6)]
  Extension request must include:
    - Entity Name - Entity DUNS Number
    - Site Name - Unit Name(s)
    - NOG Section(s) - Grounds for extension/basis for request
    - Docs from OEM re: limitations - Description of modifications
    - Schedule for implementing - Other info in Section [§2.12.1.2(2)]
  Extension ends per its terms or as approved by ERCOT [§2.12.1.2(5)]

## Slide 22: Performance Failures
Required Criteria: § 2.6.2.1; § 2.9.1; § 2.9.1.1; § 2.9.1.2 [§ 2.13(1)]
  If exemption/extension granted, documented maximum ride-through capabilities is performance requirement [§ 2.13(2)]
On performance failure
  Investigate, report cause to ERCOT, validate model, and report results to ERCOT [§ 2.13(3)]
  Develop mitigation plan, submit to ERCOT, and implement approved plan w/n 180 days [§ 2.13(5)]
For performance failure where system conditions at POIB exceeded Required Criteria but remained below maximized capabilities that exceeded Required Criteria, ERCOT will report to ERM only if RE does not meet § 2.13(3) and (5)

## Slide 23: Exemption/Extension Process - § 2.12.1
Applies if Resource cannot meet § 2.6.2.1(1)-(5); § 2.9.1(5)-(7); § 2.9.1.1(9); or § 2.9.1.2(1)-(7) [§ 2.12.1(1)]
Must submit request by 4/1/25 [§ 2.12.1(1)]
For pre-8/1/24 Resource, must accompany IFRTCR/ IVRTCR [§ 2.12.1(2)]
No new requests for newly identified technical limitations accepted after 4/1/25 [§ 2.12.1(2)]
Exemption request may be supplemented only additional info per new NOGRR to be developed [§ 2.12.1(2)]
ERCOT will grant extension if all are met: [§ 2.12.1(4)]
  Circumstances beyond entity’s control prevented meeting deadline
  Request demonstrates entity’s good faith efforts to minimize duration
  Entity provided accurate models w/ description of all limitations and limitations it cannot model and represents model is accurate
  Extension for Resource before 8/1/24 does not exceed 12/31/27
  Extension for Resource post 8/1/24 does not exceed 12/31/28

## Slide 24: Exemption/Extension Process - § 2.12.1
For Resource w/ approved exemption/extension, max capabilities become performance criteria until it ends [§ 2.12.1(4)]
Exemption/Extension becomes effective on ERCOT approval and apply on to extent approved [§ 2.12.1(5)]
Exemptions continue until Resource fully implements modification per Planning Guide § 5.2.1(1)(c) or Resource fully implements modification eliminating need for exemption [§ 2.12.1(6)]
If ERCOT or entity learns of new SFSP modification, RE must: (i) submit implementation plan w/n 90 days, and (ii) if ERCOT approves it, implement w/n 180 days [§ 2.12.1(7)]
Extensions end per § 2.12.1.2 [§ 2.12.1(8)]
Until exemption/extension/appeal is final, pre-8/1/24 AGIA Resource must meet greater of: (i) max capability, or (ii) requirements in effect on 5/1/24 [§ 2.12.1(10)]

## Slide 25: Extension Timeline - § 2.12.1.3
ASAP after receiving request, ERCOT will provide written confirmation of receipt and notification that either: (a) submission was complete; or (b) submission was incomplete and will identify missing information and provide instructions to submit missing information [§ 2.12.1.3(1)]
Within 10 Business Days of notice of incomplete submission, entity will provide missing info or request additional time w/ explanation for delay Within 7 days of receiving complete request, ERCOT will designate a Sr. rep to participate in discussions re: request
Requesting entity will cooperate in providing add’l info
ERCOT will try to complete process w/n 180 days or will provide estimate of time needed

## Slide 26: Extension Timeline - § 2.12.1.3
ERCOT will provide notification it completed review the determination of: approved; approved in part (w/ detailed explanation for denial); or rejected (with details of reason for rejection)
Aggrieved entity may appeal decision to PUCT per P.U.C. PROC. R. 22.251
If now appeal, entity deemed to have accepted decision
  NOTE: No exemption timeline described because it will be developed in subsequent NOGRR

## Slide 27: Questions?