## Slide 1: CARD and CRRBA Allocation to Entities that pay TCOS (4-CP)
Shams Siddiqi, Ph.D.
City of Georgetown Utilities
(512) 619-3532
shams@crescentpower.net
WMS Meeting
November 6, 2024

## Slide 2: Background
NPRR1030 addressed the incentive for DC Tie exports to be scheduled during monthly Coincident Peak (CP) intervals to generate an increased share of the CARD and CRRBA payments.
ERCOT is concerned that the same issue now exists for loads that are more flexible and controllable.
Since Transmission Cost of Service (TCOS) is allocated to Load on Summer 4-CP and TCOS greatly exceeds CARD and CRRBA, this issue currently does not exist during the Summer months.
Allocation using any other method than CP for the Summer months actually creates perverse incentives and RT energy price distortions that will inefficiently impact the behavior of price sensitive Load. As little as $10/MWh CARD and CRRBA artificial price increase may result in modified LFL responses
Sending such distorted energy prices and then admonishing Entities not to respond to such price signals is terribly flawed market design.
NPRR1030 added the following flawed provision in the Protocols:
  “Market Participants shall not engage in DC Tie export transactions that are reasonably expected to be uneconomic in consideration of all costs and revenues associated with the transaction, excluding CRR Auction Revenue Distribution (CARD) and CRR Balancing Account (CRRBA) allocations.”

## Slide 3: Obvious Solution (No Analysis Needed!)
There is an obvious solution that eliminates price distortion caused by CARD and CRRBA while also minimizing 4-CP allocation price distortion:
Allocate CARD and CRRBA using the same Allocation as TCOS – i.e., allocate CARD and CRRBA using 4-CP Allocation
This is also the most equitable solution – Entities that pay for the transmission system receive the benefits of CARD and CRRBA
All other proposals to date further reward 4-CP avoidance and not paying towards TCOS by not allocating CARD and CRRBA on CP basis for Summer months – worsening price distortion with no justification. Flawed provision in 1030 would be implied for whatever hours CARD and CRRBA are allocated.
Apart from 4-CP, any other allocation in non-Summer months significantly distorts energy prices in those hours and would require flawed provisions to prevent inefficiencies from economic price response – makes no sense!
Allocating using 4-CP greatly reduces the incentive for chasing 4-CP and for generation and load netting
This is the market’s opportunity to minimize the price distortion of 4-CP and eliminate any price distortion from CARD and CRRBA allocation – this is a no-brainer – no additional analysis is required!

## Slide 4: Details of COG Proposed Solution
CARD/CRRBA allocation using the 4CP method (prior-year 4CP) is:
Pull load by LSE for the prior-year four summer 4CP intervals (excluding DC Tie exports, BLT Exports & WSL). [Note: no change to NPRR1030 allocation of CARD/CRRBA for DC Tie exports since transmission charge is a flat hourly rate for the entire year for DC Tie exports]
Remove LSE data for terminated LSEs.
Add a QSE attribute to the data based upon current LSE to QSE relationship.
Aggregate 4CP load volumes by QSE.
Create QSE level 4CP Load Ratio Share (LRS) (each QSE’s Settlement extracts will show the allocation at LSE level as well).
Allocate monthly CARD/CRRBA to QSEs based on this QSE-level 4CP LRS.

## Slide 5: Related Stakeholder Consideration
Zonal/Non-Zonal CARD allocation was adopted with Nodal Market implementation due to the concerns at that time that North Load Zone prices would be elevated due to intra-zonal congestion and so, the allocation of intra-zonal CRR revenues on a Zonal basis would reduce the impact on North Load Zone load of moving to a Nodal Market
The more recent experience of allocating roughly 35% of Zonal CARD to the West Load Zone which also has low energy prices was not contemplated at the time – the large intra-zonal congestion in the West Congestion Zone is due mostly to Resources in the West using CRRs to hedge to the West Hub
On the other hand, load in the West Load Zone is only allocated about 13% of TCOS through the 4CP charge
Thus, although TCOS is more than double of CARD/CRRBA amounts in total, West Load Zone allocated TCOS is roughly 33% greater than allocated CARD/CRRBA using 4CP
Stakeholders need to consider allocating all CARD/CRRBA on a system-wide basis thereby eliminating Zonal allocation of intra-zonal CRR revenues