## Slide 1
Node Breaker Validation Rule Progress
Jessica Hernandez
Network Model Administration
11/19/24

## Slide 2: Why are we adding new validation rules?
Steady-State Working Group (SSWG) Planning models
  Transitioned from bus-branch to node breaker.
Power System Simulator for Engineering (PSSE) and Model on Demand (MOD)
  Data format requirements.
Topology Processor (TP)
  Prevent data errors.
  Prevent missing topology
  Deconsolidating loads and shunts.
NMMS
TP
PSSE & MOD
SSWG Planning Models
Rule Type | Description
Require | Require a non-null PSSEID value.
Range | Verify PSSEID is within a specified numeric or alphanumeric range.
Unique | Verify PSSEID is unique per the object type criteria

## Slide 3: Node Breaker Validation Rule Status
All templates updated
Bulk update in progress - email sent out on 11/15/24
Complete
  ShuntCompensatorALT, ShuntCompensator, and Substation.
Partially complete
  ConnectivityNode, Breaker, and Disconnector.
Pending
  One terminal connectors.
  Two terminal connectors.
Object Type | Require | Range | Unique
ShuntCompensatorALT |  |  | -
ShuntCompensator | - |  | -
Substation |  |  | 
ConnectivityNode | Pending |  | Pending
Breaker | Pending |  | -
Disconnector | Pending |  | -
One terminal | - | - | Pending
Two terminal | - | - | Pending

## Slide 4: Remaining Rules
Object Type | Attribute | Rule Description | Criteria
ConnectivityNode | PSSEID | Verify the PSSEID attribute is populated for the ConnectivityNode object type. | Not blank
 |  | Verify the PSSEID is unique for all ConnectivityNode within the substation. | Unique within the substation
Breaker | PSSEID | Verify the PSSEID attribute is populated for the Breaker object type. | Not blank
Disconnector | PSSEID | Verify the PSSEID attribute is populated for the Disconnector object type. | Not blank
Synchronous Machine | PSSEID | Verify the PSSEID is unique for SynchronousMachine object types within the ConnectivityNodeGroup. | Unique within the ConnectivityNodeGroup
CustomerLoad NonConformLoad | PSSEID | Verify the PSSEID is unique for Load object types that are under the same connectivityNodeGroup. | Unique within the ConnectivityNodeGroup
Fixed Shunt | PSSEID | Verify the PSSEID is unique for devices of the same equipment type under the same connectivityNodeGroup. | Unique within the ConnectivityNodeGroup
Switch Shunt SVC | PSSEID | Verify the PSSEID is unique for devices of these equipment type under the same connectivityNodeGroup. | Unique within the ConnectivityNodeGroup
ACLineSegment SeriesCompensator Breaker Disconnector | PSSEID | Verify the PSSEID is unique for object types that are in parallel i.e., if more than one (1) of these object types connects to the same two (2) connectivityNodeGroups. | Unique PSSEIDs for object types in parallel

## Slide 5: Questions?