## Slide 1
Monthly Review of Reliability Unit Commitment Market Impacts – October 2024
Wholesale Market Working Group
ERCOT Market Analysis

## Slide 2: RUC Resource-Hours
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.
October 2024 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 268.0 | 20.0 | 248.0
Effective Resource-Hours* |  |  | 
Total Count | 257.1 | 19.6 | 237.5
Average Megawatts (MW) for Effective Resource Hours |  |  | 
Average LSL | 73.3 | 168.7 | 65.4
Average LDL | 78.7 | 185.9 | 69.8
Average BP | 82.7 | 204.5 | 72.5
Average HSL | 208.6 | 299.4 | 201.0

## Slide 3: RUC Instruction Reasons: Last 13 Months RUC instructions in October 2024 were primarily to resolve congestion but also to ensure sufficient capacity.

## Slide 4: RUC Instruction Reasons in October 2024
257.1 RUC effective Resource-hours.
  110.2 hours (42.85%) for capacity.
  146.9 hours (57.15%) for congestion.

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months October 2024 had a total of 237.5 non-opt-out effective Resource-hours (92.38%) and 19.6 opt-out effective Resource-hours (7.62%).

## Slide 6: Non-opt-out and Opt-out Totals: October 2024

## Slide 7: RUC Lead Time Margin: October 2024
Lead time refers to the length of time between a RUC instruction and the start of the commitment window.
Lead time margin is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.
All RUC commitment windows had a lead time margin at or below 8 hours.

## Slide 8: Average Resource Age: Last 13 Months In October 2024, the average age of RUC-committed Resources was 52.2 years for non-opt-out Resource-hours and 68.8 years for opt-out Resource-hours without DAM Commitments and 12.9 for opt-out Resource-hours with DAM Commitments.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months Most RUC-committed Resources in October 2024 were more than 50 years old.
Non-opt-out
Opt-out

## Slide 10: RUC-Instructed Resource Dispatch above LDL
October 2024
There were 12.4 effective Resource-hours in which Resources that did not successfully opt out were dispatched above their LDL.
  For 1.3 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 11.1 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    Of these 11.1 Resource-hours, 10.7 Resource-hours were mitigated.
There were no Exceptional Fuel Cost submissions for any RUC-committed Resources.

## Slide 11: Reliability Deployment Price Adder: Last 13 Months October 2024 had a total of 145.85 RTORDPA hours with an average value of $0.91/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder: October 2024 OD 10/09 had the highest daily time-weighted average RTORDPA of $3.42/MWh.
Note:
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for more details.
2. The non-zero RTORDPA in grey bar on OD 9/29 was triggered by NCLR Non-Spin Deployment.

## Slide 13: RUC Clawback, Make-Whole, and Shortfall For October 2024, the total Clawback Charge was $197,331. The total Make-Whole Payment was $321,342.
Of the $321,342 in Make-Whole Payments made in October 2024, $5.57 was uplifted to load due to rounding.
The remaining amount was collected through Capacity-Short Charges.
Data as of November 8th, 2024

## Slide 14: RUC Clawback by Settlement Type
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of November 8, 2024 ($)
Oct ‘23 | 190,721 | 0 | 0 | 190,721
Nov ‘23 | 29,684 | 0 | 0 | 29,684
Dec ‘23 | 0 | 0 | 0 | 0
Jan ‘24 | 107,176 | -4,657 | 0 | 102,519
Feb ‘24 | 88,220 | 0 | 0 | 88,220
Mar ‘24 | 487,193 | 0 | 0 | 487,193
Apr ‘24 | 2,092,224 | 0 | -11,819 | 2,080,406
May ‘24 | 2,084,416 | 0 | - | -
Jun ’24 | 58 | 0 | - | -
Jul ‘24 | 47,627 | 0 | - | -
Aug ‘24 | 73,690 | 0 | - | -
Sep ‘24 | 140,239 | - | - | -
Oct ‘24 | 179,331 | - | - | -
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.

## Slide 15: RUC Make-Whole by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of November 8, 2024 ($)
Oct ‘23 | -72,477 | -43,063 | 0 | -115,540
Nov ‘23 | -194,731 | 0 | -17,934 | -212,665
Dec ‘23 | -5,316 | 0 | 0 | -5,316
Jan ‘24 | -253,466 | -79,942 | 31,417 | -301,991
Feb ‘24 | -19,673 | 0 | -9,004 | -28,677
Mar ‘24 | -353,562 | 0 | 0 | -353,562
Apr ‘24 | -443,178 | 0 | -35,271 | -478,449
May ‘24 | -2,957 | 0 | - | -
Jun ’24 | -76,670 | 0 | - | -
Jul ‘24 | -4,297 | 0 | - | -
Aug ‘24 | -305,171 | 0 | - | -
Sep ‘24 | -239,681 | - | - | -
Oct ‘24 | -364,395 | - | - | -