## Slide 1: CARD and CRRBA Allocation to Entities that pay TCOS (4-CP) & Transition to System-Wide CARD
Shams Siddiqi, Ph.D.
City of Georgetown Utilities
(512) 619-3532
shams@crescentpower.net
WMWG Meeting
December 10, 2024

## Slide 2: Background
ERCOT is concerned that flexible and controllable load will increase consumption during monthly Coincident Peak (CP) intervals to generate an increased share of the CARD and CRRBA payments.
Since Transmission Cost of Service (TCOS) is allocated to Load on Summer 4-CP and TCOS greatly exceeds CARD and CRRBA, this issue currently does not exist during the Summer months.
Allocation using any other method than CP for the Summer months actually creates perverse incentives and RT energy price distortions that will inefficiently impact the behavior of price sensitive Load. As little as $10/MWh CARD and CRRBA artificial price increase may result in modified LFL responses
Sending such distorted energy prices and then admonishing Entities not to respond to such price signals is terribly flawed market design.

## Slide 3: Obvious Solution (No Analysis Needed!)
There is an obvious solution that eliminates price distortion caused by CARD and CRRBA while also minimizing 4-CP allocation price distortion:
Allocate CARD and CRRBA using the same Allocation as TCOS – i.e., allocate CARD and CRRBA using 4-CP Allocation
This is also the most equitable solution – Entities that pay for the transmission system receive the benefits of CARD and CRRBA
All other proposals to date further reward 4-CP avoidance and not paying towards TCOS by not allocating CARD and CRRBA on CP basis for Summer months – worsening price distortion with no justification.
Apart from 4-CP, any other allocation in non-Summer months significantly distorts energy prices in those hours and would result in inefficient LFL behaviour – makes no sense!
Allocating using 4-CP greatly reduces the incentive for chasing 4-CP and for generation and load netting
This is the market’s opportunity to minimize the price distortion of 4-CP and eliminate any price distortion from CARD and CRRBA allocation – this is a no-brainer – no additional analysis is required!

## Slide 4: Cap Allocation of Zonal CARD to TCOS
Eliminating Zonal CARD allocation in favor of system-wide CARD allocation would be a sudden huge redistribution of CARD between the Zones
As shown in ERCOT analysis, 4CP method is by far the closest allocation to the current allocation without any CARD related energy price distortion
Thus, in order for the COG proposal to maintain the current distribution of CARD as closely as possible and gradually transition to system-wide CARD allocation:
  Cap CARD allocation to any Zone by its allocation of TCOS
  Once the CARD allocation cap is reached in one or more Zones within a year, distribute CARD to the Zones that have not reached their caps for the remainder of the year
  [System is far from reaching this milestone – so maybe addressed in a separate NPRR if needed in the future] Once all Zones reach their CARD allocation cap, distribute CARD on a monthly system-wide LRS for the remainder of the year

## Slide 5: Details of COG Proposed Solution
CARD/CRRBA allocation using the 4CP method (prior-year 4CP) is:
Pull load by LSE for the prior-year four summer 4CP intervals (excluding DC Tie exports, BLT Exports & WSL). [Note: no change to NPRR1030 allocation of CARD/CRRBA for DC Tie exports since transmission charge is a flat hourly rate for the entire year for DC Tie exports]
Remove LSE data for terminated LSEs.
Add a QSE attribute to the data based upon current LSE to QSE relationship.
Aggregate 4CP load volumes by QSE.
Create QSE level 4CP Load Ratio Share (LRS) (each QSE’s Settlement extracts will show the allocation at LSE level as well).
Allocate monthly CARD/CRRBA to QSEs based on this QSE-level 4CP LRS.
Transition to system-wide CARD allocation by capping CARD allocation for each Zone based on that Zone’s TCOS allocation

## Slide 6: Comparison of Competing Proposals
Feature | COG Proposal | Vistra Proposal | IMM Proposal
Shifting of CARD allocation from Residential/NOIE to Large C&I | 0% | 3% (based on IMM estimate for about 100 hours/month) | 6% (based on IMM estimate)
Energy Price Distortion to chase CARD outside 4CP | $0/MWh | As high as $40/MWh (for Load - effectively reduces LZ SPP by this amount) | As high as $10/MWh (for Load - effectively reduces LZ SPP by this amount)
Maintain Zonal CARD Allocation but transition to system-wide LRS | Yes - Transition to system-wide LRS through Zonal caps | No – maintains current Zonal CARD distribution | No – maintains current Zonal CARD distribution
Reduces incentive to avoid 4CP and net Gen & Load | Yes | No – actually increases 4CP chasing incentive | No – actually increases 4CP chasing incentive