## Slide 1
Annual Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2024
Ryan King
Manager, Market Design
TAC
January 22, 2025
ERCOT Public

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: Key Observations for 2024
Overall reduction in the amount of RUC observed in 2024 (~1,800 Resource-hours) v. 2023 (2,500 Resource-hours) and significantly below 2022 (7,900 Resource-hours). Factors that may have contributed to this trend include:
  General changes in Resource-owner real-time price expectation
  Lower average fuel prices compared to 2023
  Additional On-Line capacity from Solar and Energy Storage Resources
April and October had the highest and second highest amount of RUC activity
  Not concentrated on certain days but distributed over several days throughout the month
Higher incidences of RUC observed in the 4th quarter of 2024 compared to the same period in 2023
Change in the composition of RUC in 2024 compared to 2023
  RUC Resource-hours for local thermal congestion or voltage concerns were roughly 1/3 of total in 2024 compared to ~3% in 2023
  RUCs for congestion concentrated in the last 3 months of 2024
  Note: Any Resource committed to help congestion also naturally helps with capacity

## Slide 4: RUC-Instructed Resource-Hours in 2024
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Capacity |  | Congestion | 
 |  | Opt-Out | Non-Opt-Out | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  |  |  | 
Total Count | 1,976.0 | 85.0 | 1,152.5 | 38.0 | 700.0
Effective Resource-Hours* |  |  |  |  | 
Total Count | 1,860.9 | 80.7 | 1,076.9 | 37.9 | 665.4
Average LSL | 102.8 | 154.4 | 105.6 | 72.7 | 93.7
Average LDL | 114.1 | 207.1 | 108.5 | 147.3 | 110.0
Average BP | 119.2 | 242.8 | 110.1 | 186.5 | 115.1
Average HSL | 281.8 | 333.2 | 312.9 | 239.7 | 227.6

## Slide 5: RUC Instruction Reasons
1,860.9 effective RUC Resource-hours in 2024.
  703.3 Resource-hours (37.8%) for local thermal congestion or voltage concerns.
  1,157.6 Resource-hours (62.2%) for capacity concerns.
There were no Resource-hours committed for Ancillary Service shortages, system inertia, or startup failures.
118.6 effective Resource-hours (6.3%) were successfully bought back.
  This value is much less than last year (20.4% bought back in 2023).
  Included in this value are 66.7 effective Resource-hours (3.6% of total) where the Resource was DAM-committed.

## Slide 6: RUC-Effective Resource-Hours, 2021 - 2024

## Slide 7: RUC-Effective Resource-MWh, 2021 - 2024
Top: Duration multiplied by Resource’s Base Point (BP).
Bottom: Duration multiplied by Resource’s High Sustained Limit (HSL).

## Slide 8: Average Age of Effective Resource-Hours, 2021 - 2024
In the case of Resources with multiple physical generators, the age of the oldest generator is used.

## Slide 9: RUC-Effective Resource-Hours by Resource Age, 2021 - 2024
OPT-OUT
.
NON-OPT-OUT

## Slide 10: RUC-Effective Resource Dispatch above LDL
When Resources did not successfully opt out, there were 143.4 Resource-hours when the Resource was dispatched above its LDL.
  For 58.2 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 85.3 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For 83.9 of these Resource-hours, the RUC-instructed Resource was mitigated.
    There were 23.1 Resource-hours associated with a RUC for additional capacity.
    There were no Resource-hours for which a non-mitigated RUC-instructed Resource was DAM-committed. (Hours meeting these criteria are treated as a RUC opt out.)

## Slide 11: Reliability Deployment Price Adder
Month of 2024 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 54.25 | 7.77
Feb | 15.67 | 2.50
Mar | 190.26 | 1.13
Apr | 195.39 | 2.32
May | 41.59 | 2.24
Jun | 54.00 | 0.93
Jul | 15.01 | 1.86
Aug | 67.25 | 1.93
Sep | 49.33 | 1.56
Oct | 145.85 | 1.32
Nov | 70.44 | 2.33
Dec | 167.83 | 0.89
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: RUC Make-Whole and Claw Back, 2021 - 2024
$2.67M in Make-Whole paid out over the year. Only $25.20 uplifted to Load. Settlement data retrieved 01/15/2025.

## Slide 13: Exceptional Fuel Cost Submissions
No resources with RUC instructions reported exceptional fuel costs.

## Slide 14: Additional Observations
In 2024, 1,976 instructed RUC Resource-hours resulted in 1,860.9 effective RUC Resource-hours.
  As compared to 2,726 and 2,500.6 for 2024, respectively.
  6.3% of effective resource-hours were bought back.
The total RUC make-whole amount was ~$2.67M.
  Almost exclusively covered through capacity-short charges.
The total RUC claw back charge amount was ~$7.4M.
Settlement data retrieved 01/15/2025.

## Slide 15: Appendix

## Slide 16: RUC-Instructed Effective Resource-Hours by Opt Out Status*
Month | 2021 | 2022 | 2023 | 2024
Jan | 5 | 80 | 167 | 112
Feb | 5 | 930 | 249 | 20
Mar | 5 | 200 | 147 | 224
Apr | 8 | 328 | 362 | 400.5
May | 0 | 382 | 445 | 74
Jun | 248 | 511 | 309 | 73
Jul | 968 | 672 | 114 | 22
Aug | 378 | 870 | 11 | 171
Sep | 339 | 1,124 | 74 | 121
Oct | 573 | 305 | 33 | 246
Nov | 107 | 517 | 73 | 159.5
Dec | 11 | 381 | 7 | 230
Month | 2021 | 2022 | 2023 | 2024
Jan | 0 | 26 | 99 | 28
Feb | 269 | 62 | 0 | 0
Mar | 24 | 62 | 38 | 0
Apr | 63 | 163 | 42 | 25
May | 0 | 219 | 102 | 0
Jun | 89 | 108 | 31 | 15
Jul | 229 | 236 | 67 | 0
Aug | 203 | 176 | 2 | 13
Sep | 139 | 225 | 41 | 0
Oct | 102 | 106 | 12 | 20
Nov | 73 | 209 | 76 | 17
Dec | 14 | 19 | 0 | 5
Did Not Opt Out
Opted Out
* Effective Resource-hours rounded to nearest whole number

## Slide 17: RUC Make-Whole and Claw Back, 2021-2022
Amounts rounded to nearest thousand. Settlement data retrieved on 01/15/2025.
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2021 | 2022 | 2021 | 2022 | 2021 | 2022 | 2021 | 2022 | 2021 | 2022
Jan | 0 | -320 | 0 | 320 | 0 | 0 | 1 | 38 | 0 | 3,760
Feb | 0 | -6,970 | 0 | 6,970 | 0 | 0 | 1,256 | 7,628 | 0 | 7,519
Mar | -9 | -749 | 9 | 749 | 0 | 0 | 6 | 102 | 239 | 6,203
Apr | -19 | -742 | 19 | 742 | 0 | 0 | 0 | 1,285 | 263 | 7,138
May | 0 | -3,302 | 0 | 3,302 | 0 | 0 | 0 | 7,293 | 0 | 10,604
Jun | -466 | -6,014 | 466 | 6,014 | 0 | 0 | 91 | 12 | 7,004 | 17,784
Jul | -2,045 | -9,841 | 2,045 | 9,841 | 0 | 0 | 637 | 5,245 | 17,403 | 17,799
Aug | -865 | -13,274 | 865 | 13,274 | 0 | 0 | 59 | 110 | 12,650 | 15,788
Sep | -833 | -8,806 | 832 | 8,806 | 0 | 0 | 54 | 208 | 11,833 | 20,310
Oct | -888 | -3,675 | 888 | 3,675 | 0 | 0 | 893 | 80 | 10,652 | 9,482
Nov | -61 | -5,665 | 61 | 5,665 | 0 | 0 | 89 | 689 | 1,315 | 10,589
Dec | -196 | -10,768 | 196 | 10,768 | 0 | 0 | 0 | 0 | 1,106 | 6,713

## Slide 18: RUC Make-Whole and Claw Back, 2023-2024
Amounts rounded to nearest thousand. Settlement data retrieved on 01/15/2025.
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2023 | 2024 | 2023 | 2024 | 2023 | 2024 | 2023 | 2024 | 2023 | 2024
Jan | -301 | -302 | 301 | 302 | 0 | 0 | 822 | 103 | 1,886 | 2,724
Feb | -327 | -29 | 327 | 29 | 0 | 0 | 157 | 88 | 3,045 | 867
Mar | -441 | -354 | 441 | 354 | 0 | 0 | 180 | 487 | 5,695 | 4,756
Apr | -914 | -478 | 914 | 478 | 0 | 0 | 50 | 2,080 | 11,694 | 7,897
May | -470 | -3 | 470 | 3 | 0 | 0 | 364 | 2,084 | 8,601 | 952
Jun | -687 | -134 | 687 | 134 | 0 | 0 | 149 | 0 | 8,007 | 5,413
Jul | -168 | -114 | 168 | 114 | 0 | 0 | 158 | 0 | 5,138 | 1,424
Aug | -12 | -305 | 12 | 305 | 0 | 0 | 352 | 74 | 322 | 7,143
Sep | -35 | -240 | 35 | 240 | 0 | 0 | 998 | 140 | 562 | 5,141
Oct | -116 | -364 | 116 | 364 | 0 | 0 | 191 | 179 | 757 | 11,878
Nov | -213 | -164 | 213 | 164 | 0 | 0 | 30 | 2,023 | 2,554 | 4,556
Dec | -5 | -180 | 5 | 180 | 0 | 0 | 0 | 147 | 305 | 8,127