## Slide 1: Duration Requirements for Ancillary Services in RTC-SCED
Andrew Reimers, Ph.D.
Deputy Director
Potomac Economics | ERCOT IMM
RTCBTF
January 23, 2025

## Slide 2: Current Duration Requirements Raise Market and Reliability Concerns in RTC-SCED
Currently, the duration requirements are 2 hours for ECRS and 4 hours for NSPIN.
These duration requirements will tend to incentivize ESRs to provide energy rather than reserves under tight conditions
  A 100 MWh battery can sell 100 MW of energy, reg, or RRS
  In contrast, the same battery could sell only 50 MW of ECRS or 25 MW of NSPIN – this creates indifference price of 2x to 4x for these reserves relative to energy or higher-quality reserves, particularly under scarcity conditions with max energy prices
  In addition, SCED will recognize less available supply for these products, resulting in higher AS and energy prices. The higher energy prices will tend to lead to more energy awards for ESRs sooner into a reliability event
  Conversely, the higher reserve prices will tend to incentivize gas turbines to provide reserves rather than energy, because their cost for providing reserves is lower than their cost of producing energy
  Ideally, gas turbines would be dispatched for energy before duration-limited resources

## Slide 3: Separate Duration Requirements for Qualification vs. RTC-SCED is a Reasonable Short-term Approach
ERCOT could continue to use the 2 and 4 hour duration requirements for qualifying reserve capacity for ESRs
In RTC-SCED, duration requirements for ECRS and NSPIN should be set to no more than 1 hour each
This distinction avoids the worst market and reliability outcomes in SCED and allows ERCOT to aggregate reserves across multiple ESRs
Longer-term, other market design changes are needed to more effectively manage reserves provided by longer-duration resources

## Slide 4: Market Design for Reserves from Duration Limited Resources
The IMM still recommends that the current duration requirements for ECRS and NSPIN be reconsidered but respects that there are longer duration reliability events that require longer duration operating reserves
DRRS should be implemented ASAP, allowing for the duration of NSPIN to be reduced to one hour
The AS Plan for ECRS and NSPIN should be reformulated in terms of both MWs and MWhs to allow for more appropriate procurement of reserves from ESRs in real-time