## Slide 1
ASDCs for use in RUC Studies
Ryan King
Manager, Market Design
RTC+B Task Force
February 7, 2025

## Slide 2: Agenda
Recap: RUC ASDC and of RTC RUC Inputs
Recap of Non-Spin and ECRS in RUC
Outline and Review of the RUC ASDC Sensitivity Analysis
Next Steps

## Slide 3: Recap – ASDCs for RUC
NPRR 1269: RTC+B Three Parameters Policy Issues proposes the ASDCs for use in RUC be the same as those derived for the Day-Ahead Market and Real-Time Market but with the following modifications:
  ASDC for Non-Spin shall not extend beyond the AS Plan for Non-Spin
  Use of a floor price such that no values on the ASDC curve for each AS fall below $X/MWh
Floor price at the ‘tail’ of the ASDC is necessary to ensure sufficient capacity is available to meet AS Plan
ERCOT has been conducting sensitivity analysis using a developed basecase for testing in the vendor RUC engine to understand the impact of different floor prices on AS procurement.

## Slide 4: Review of RTC RUC Inputs
COP will now contain AS capabilities for each AS product (instead of AS Responsibilities today), including any subtypes for which the Resource is qualified.
Resource Name | QSE Name | Delivery Date | Delivery Hour | Status | HSL (MW) | LSL (MW) | HEL (MW) | LEL (MW) | Reg-Up (MW) | Reg-Down (MW) | RRSPFR (MW) | RRSFFR (MW) | RRSUFR (MW) | Non-Spin (MW) | ECRS (MW) | Max SOC (MWh) | Min SOC (MWh)) | Target SOC (MWh)
Resource A | QSE 1 | 1/9/2025 | 1 | ON |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Resource B | QSE 1 | 1/9/2025 | 1 | OFF |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… | … | 1/9/2025 | 1 | … |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Resource C | QSE 2 | 1/9/2025 | 1 | OUT |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Resource D | QSE 3 | 1/9/2025 | 1 | OFFQS |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: Review of RTC RUC Inputs
RUC will read the latest submitted AS Offers that are available for the study period.
Proxy AS Offers will be used in RUC in determining a co-optimized solution where AS Offers have not been submitted.
Resource Name | Resource Type | QSE Name | AS Category | Submit ID | Block ID | Delivery Date | Delivery Hour | Number Of PQ Pairs | Quantity 1 (MW) | Block Indicator 1 | URS Price 1 ($/MW) | RRSPFR Price 1 ($/MW) | RRSFFR Price 1 ($/MW) | RRSUFR Price 1 ($/MW) | ECRS Price 1 ($/MW) | ONNS Price 1 ($/MW) | DRS Price 1 ($/MW) | OFFNS Price 1 ($/MW) | OFFEC Price 1 ($/MW) | … | Quantity 5 (MW) | …
Resource A | NCLR | QSE 1 | ONRES | 123 | 0 | 1/10/2025 | 1 | 1 | 12 | V |  |  |  | 0 |  |  |  |  |  |  | 0 | 
Resource A | NCLR | QSE 1 | ONRES | 123 | 0 | 1/10/2025 | 2 | 1 | 12 | V |  |  |  | 0 |  |  |  |  |  |  | 0 | 
Resource A | NCLR | QSE 1 | ONRES | 123 | 0 | 1/10/2025 | 3 | 1 | 12 | V |  |  |  | 0 |  |  |  |  |  |  | 0 | 
Resource A | NCLR | QSE 1 | ONRES | 123 | 0 | 1/10/2025 | 4 | 1 | 12 | V |  |  |  | 0 |  |  |  |  |  |  | 0 | 
Resource A | NCLR | QSE 1 | ONRES | 123 | 0 | 1/10/2025 | 5 | 1 | 12 | V |  |  |  | 0 |  |  |  |  |  |  | 0 | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: Recap of Non-Spin and ECRS in RUC
COP STATUS | RUC STATUS | Eligible Non-Spin Award | Eligible ECRS Award
ON | ON | On-Line Non-Spin | On-Line ECRS
OFFQS | OFFQS | On-Line Non-Spin | On-Line ECRS
OFF | ON | On-Line Non-Spin | On-Line ECRS
OFF | OFF | Off-Line Non-Spin | NO

## Slide 7: Outline of the HRUC study save case
Purpose: Sensitivity analysis compares penalty of the shortage v. commitment cost
Higher penalty (ie higher AS floor price) increases penalty of shortage relative to commitment cost
Basecase 1: Load forecast based on ERCOT Dec 2024 Mid-Term Load Forecast (MTLF)
Basecase 2: MTLF and adjusted with Peak load around 70,000 MW.
Basecase 2a: Inclusion of ASDC Floor Price of $50 applied to Basecase 2
Production (Dec 2024) network model.
ERCOT proposed ASDC curve.
Production (Dec 2024) COP data was used with updated AS Capability.

## Slide 8: Interpreting Results
Including of a price floor:
  Allows RUC optimization to make different commitment decisions than initial Basecase
  Not necessarily committing more HSL capacity, but the change in the units committed enables previous capacity to be considered for Off-Line Non-Spin awards

## Slide 9: Base Case Analysis Results
 | On-Line NSPIN Award (MW) | Off-Line NSPIN Award (MW) | Total NSPIN Award (MW) | NSPIN Shortage (MW) | NSPIN Shadow Price ($) | Unit Commit Unit # | Unit Commit HSL (MW) | Total Commitment Cost ($)
Case 1 | 2334.9 | 829.04 | 3164 | 0 | 0 | 0 | 0 | 0
Case 2 | 126.04 | 2880.4 | 3006.44 | 157.56 | 3.27 | 37 | 3085.9 | 174,420.26
Case 2a | 110.6 | 3053.4 | 3164 | 0 | 0.12 | 40 | 3084.7 | 174,843.66
All analyses are for HE 19
AS Plan for Non-Spin: 3164 MW
Base Case 1: Load 49,302 MW
Base Case 2: Load 70,302 MW
Base Case 2a: Load 70,302 MW with $50 ASDC Price Floor

## Slide 10: Base Case Analysis
 | Basecase2a with $50 Floor Price |  | Basecase2 |  | NSPIN Award Delta (MW)
Resource Name | NSPIN Award (MW) | Generation Commitment Status | NSPIN Award (MW) | Generation Commitment Status | 
Unit_1 | 0 | ON | 12.2 | OFF | -12.2
Unit_2 | 0 | ON | 5 | OFF | -5
Unit_3 | 0 | ON | 5.1 | OFF | -5.1
Unit_4 | 0 | ON | 10.3 | OFF | -10.3
Unit_A | 56.6 | OFF | 0 | ON | 56.6
Unit_B | 149.5 | OFF | 0 | ON | 149.5
Unit_X | 34.4 | OFF | 34.9 | OFF | -0.5
Unit_Y | 0 | ON | 3.34 | ON | -3.34
Unit_Z | 39.8 | ON | 51.9 | ON | -12.1
Green highlights the Units committed under Case 2a (Units 1-4)
Orange highlights the Units committed under Case 2 (Units A, B)
Floor Price allows RUC to commit different units in Case 2a which in turn allows the HSL of Units A and B to now be considered to be awarded Off-Line Non-Spin

## Slide 11: Next Steps
Initial study indicates that a ASDC floor price in RUC will help to ensure RUC commits sufficient capacity and meet AS plan
$50 ASDC floor likely higher than required
  Initial analysis indicates a lower floor price may help resolve Non-Spin shortage
Plan to come forward with additional sensitivity analysis