## Slide 1
ASDCs for use in RUC Studies
Ryan King
Manager, Market Design
RTC+B Task Force
February 19, 2025

## Slide 2: Agenda
Recap: RUC ASDC and of RTC RUC Inputs
Feb 7 RTC+B Recap
Additional Analysis Results
Next Steps

## Slide 3: Recap – ASDCs for RUC
NPRR 1269: RTC+B Three Parameters Policy Issues proposes the ASDCs for use in RUC be the same as those derived for the Day-Ahead Market and Real-Time Market but with the following modifications:
  ASDC for Non-Spin shall not extend beyond the AS Plan for Non-Spin
  Use of a floor price such that no values on the ASDC curve for each AS fall below $X/MWh
Floor price at the ‘tail’ of the ASDC is necessary to ensure sufficient capacity is available to meet AS Plan
ERCOT has been conducting sensitivity analysis using a developed basecase for testing in the vendor RUC engine to understand the impact of different floor prices on AS procurement.

## Slide 4: Feb 7 RTC+B Recap
ERCOT presented results of analysis to understand the ability of RUC ASDCs to meet full AS Plan by testing an adjusted savecase in the RTC-RUC vendor application
  Basecase 1: Load forecast based on ERCOT Dec 2024 Mid-Term Load Forecast (MTLF) (no AS shortage)
  Basecase 2: MTLF and adjusted with Peak load around 70,000 MW. (Non-Spin shortage)
  Basecase 2a: Inclusion of ASDC Floor Price of $50 applied to Basecase 2 (No AS shortage –ie resolved with a floor)
Key Takeaways
  ASDC floor price in RUC will help to ensure RUC commits sufficient capacity and meet AS plan
  Price floor allows RUC optimization to make different commitment decisions than initial Basecase
  Not necessarily committing more HSL capacity, but the change in the units committed enables previous capacity to be considered for Off-Line Non-Spin awards

## Slide 5: Additional Analysis
$50 price floor likely higher than required to resolve Non-Spin shortage within RUC optimization
Next slides outline additional sensitivity analyses using floor values

## Slide 6: Interpreting Results
Complex interdependencies in RUC
  RUC recommendations using a given savecase may not be identical or completely intuitive (in terms of units committed and commitment cost) due to mixed-integer problem solving complexity and iteration within a timely and efficient solving process
  Some variation in results can occur within a convergence tolerance to meet objective function
Focus on savecase results illustrate ability of RUC to resolve AS shortages while meeting overall cost-minimization objective

## Slide 7: Analysis Results
 | Hour 19 System Load (MW) | NSPIN AS Plan (MW) | NSPIN Shortage (MW) | Online NSPIN Award (MW) | Offline NSPIN Award (MW) | NSPIN Shadow Price ($) | Commit Unit # | Commitment Unit HSL
Base Case 2 | 70302 | 3164 | 108.3 | 116.6 | 2939.1 | 2.83 | 40 | 3086.1
Base Case 2 with $10 Floor Price | 70302 | 3164 | 18.82 | 118.88 | 3026.3 | 10 | 40 | 3086.8
Base Case 2 with $15 Floor Price | 70302 | 3164 | 0.51 | 106.78 | 3056.7 | 15 | 40 | 3087.1
Base Case 2 with $20 Floor Price | 70302 | 3164 | 0 | 110.2 | 3053.8 | 0.12 | 40 | 3089.5
Results (all for Hour 19) indicate that the AS Shortage can be resolved with a ASDC floor ~$15

## Slide 8: Next Steps
Review additional savecases to test and inform a recommended ASDC price floor for use in RUC studies (and reflected in NPRR 1269)